## Slide 1: AURIX™ TC2xx Product Overview
IFAG ATV MC

## Slide 2: Table of contents
Infineon Microcontroller
1
  3
AURIX TC2xx PDH Support model
2
  14
AURIX TC2xx Overview
3
  17
AURIX TC2xx Feature Details
4
  31
AURIX TC2xx Functional Safety
5
  51
AURIX TC2xx Security
6
  64
AURIX TC2xx Powertrain
7
  75
AURIX TC2xx xEV
8
  79
AURIX TC2xx CAV
9
  110
AURIX TC2xx Benchmarking vs. Competition
10
  118
AURIX TC2xx SW & Tools
11
  127

## Slide 3: Table of contents
Infineon Microcontroller
1
3
AURIX TC2xx PDH Support model
2
  14
AURIX TC2xx Overview
3
  17
AURIX TC2xx Feature Details
4
  31
AURIX TC2xx Functional Safety
5
  51
AURIX TC2xx Security
6
  64
AURIX TC2xx Powertrain
7
  75
AURIX TC2xx xEV
8
  79
AURIX TC2xx CAV
9
  110
AURIX TC2xx Benchmarking vs. Competition
10
  118
AURIX TC2xx SW & Tools
11
  127

## Slide 4: TriCore™ based Infineon Automotive MCUs 1 Architecture, 3 Functions, 5 generations
Chart: 
| 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017
Audo1 | 2 | 1.345 | 0.3134 | 0.16305 | 0.14063 | 0 | 0 | 0 | 0 | 0 | 0
AudoS | 0.5 | 0.8 | 1 | 1.2 | 1.38 | 1.4 | 1.4 | 1.3 | 1.3
AudoNG | 1.4575 | 4.7024 | 9.469 | 14.283 | 19.611 | 15.853 | 13.7131 | 14.4548 | 10.0589 | 7.4779 | 4.4541
AudoFuture | 0.011161 | 0.24878 | 3.0583 | 11.5231 | 17.3057 | 19.8512 | 24.2488 | 21.5226 | 17.8688 | 12.5311
AUDOMAX | 0 | 0 | 0.042935 | 0.40989 | 2.7036 | 9.4291 | 22.682 | 34.824 | 42.6899
AURIX | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.001 | 0.045061 | 0.77013 | 6.1252
Used in
> 50
car brands
Audo 1
Audo NG
Audo Future
AUDO MAX
AURIX TC2xx
AURIX TC3xx
TriCoreTM integrates three functions: DSP, RISC & Microcontroller
1999, TriCoreTM concept born
2005, TriCoreTM goes production
2012, TriCoreTM announced 5th generation: AURIXTM
2017, TriCoreTM hits 350mil. shipment
>450,000,000
TriCore MCUs shipped
>10,000,000
AURIX on the road
>30%
Engine control market share
Made for
Powertrain
ADAS
Safety
Connectivity

## Slide 5: Continuous Market success with TriCore™ in Powertrain Worldwide #1 position
2016 TriCore market share
Transmission Control
Chart: 
| TriCore | Others
Sales | 19 | 81
Source: IFX assessment, market figures based on IHS main controller for ECU and TCU only
* incl. (H)EV inverter control
2016 TriCore market share
Engine Management System*
Chart: 
| TriCore | Others
Sales | 39 | 61
Increasing market share expected in Engine due to superior AURIX performance, first major Design Wins with AURIX 2nd Generation
Increasing production volume for Japanese and Chinese Tier1 for various OEMs

## Slide 6: AURIX™ for Powertrain Micro-controller Nr. 1 in Engine, Grow fast with E-mobility
>450 Million 32bit TriCoreTM solutions in the market
#4 WW in Automotive Microcontroller
Powertrain #1
Chassis & Safety
Driver Assistance
Advanced Body
Fully committed to the Automotive Business
High Quality Track-record
xEV
Security
Safety
EMS
AURIX can be found in everywhere in (H)EV cars from Inverter, BMS to DC-DC converter & On-board-charger
In-Vehicle Network
Tuning and Theft Protection
Automotive Safety
Strongest competence, growing with leading tier1s in GDI, DDI & MPI
Starter Stop
Driving Dynamic
Sailing, Coasting
Model predictive control
Vehicle Energy Management for efficiency and dynamics
Cost competitiveness Automotive Quality Long-term Availability
Our Success story
Our Powertrain Growth Vectors
Domain
Control
AURIX product portfolio successfully positioned in the Safety & Radar domain, also Vehicle controlling & Hybrid controlling
TCU
Automatic (DCT, CVT, ECAT, AMT)
eClutch
4WD & AWD with Torque Control

## Slide 7: AURIX™ - Automotive focus applications A trusted architecture in key application domains
AURIX™ decided/discussed for key projects at all key OEMs
requiring
a combination of high real-time performance, ASIL-D capabilities and latest security features
Infotainment, V2x, Smart cockpit, telematics, HUD, wireless charging, HVAC, sound generator

## Slide 8: AURIXTM – scalable family setting Trends
AURIXTM – Safety joins Performance
Long-term Supply Availability and Supply Security
Automotive Quality Standards
  Performance
  Functional Safety and Security
  Scalability
  Enablement
  Platform Safety Concept: ISO26262,IEC61508, ISO25119 compliant
  32-bit Programmable Security Hardware
  Pinout compatibility
  Various packages
  Scalable HW:
  1-3 TriCoreTM cores 133-300MHz
  512k – 8MB Flash
  48k -2.7MB RAM
  Expert tools
  Free Tool Chain
  Technical experts
  Reference designs
  Preferred Design House Support
  Multi-core technology
  HW accelerators
  Floating-point Unit
  Up to 2.3 DMIPS/MHz
Notes: Infineon reached levels of below 1ppm for overall MCU portfolio as well as for leading edge 32bit controllers

## Slide 9: AURIX™ for ICE and eMobility
Airbag
Braking
Steering
Radar
Data Fusion
Gateaway/Telematics
Domain Control
Data Fusion
Braking
Steering
Braking
Steering
Radar
Domain Control
Vision 2D/3D
Gateaway/Telematics
Engine Management
System
AUDOMAX
AURIX™
TC2xx
AURIX™
TC3xx
AURIX ™
TC4xx
Engine Management
System (GDI/DDI)
Transmission
Hybrid
Engine Management
System (GDI/HEV)
Hybrid
Engine Management
System
Hybrid
Transmission
Transmission
Transmission
SoP 2015 – 2020+
SoP 2019 – 2024+
SoP 2022 – 2026+
0.5-8MByte
3x Multi-core
1-16MByte
6x Multi-core
1.5-4MByte
Single core
Production
2-32MByte
Multicore & GHz processing
Hybrid
Domain Control
Domain Control
Airbag
Airbag
Radar
Data Fusion
Gateaway/Telematics
Clean
Safe
Smart
Main Market Drivers:
Fuel Efficiency
Autonomous Vehicles
Connected Car

## Slide 10: Flash Technology Process Roadmap Second Source Concept secures continuous supply
Technology Phase Out
Automotive Qualification
C9 0.22/0.25um
C11FLA, 130nm
L90FLA, 90nm
C65FLA, 65nm
C40FLA, 40nm
Multi-Core
Single-Core
2020
2005
2010
2015
2025
DRESDEN
DRESDEN
TSMC
2nd Source TSMC
2nd Source Fab14/Fab12
2nd Source SIN/DRS
TSMC
Global Foundries
DRESDEN
XC166 & XC800 families
AUDO-NG / AUDO-F & XC2000 families
AUDO-Max TC1700 family
AURIX™ - TC2xx family (in prod./qual.)
AURIX™ 2G – TC3xx family (in development)
C2xFLA, 2xnm
In development
AURIX™ 3G
32-bit TriCore microcontroller

## Slide 11: Infineon Automotive Multi-Site Concept for Frontend Operations
90nm
eFlash
65nm
eFlash
AMKOR
ASE
Infineon
Global Foundries
Infineon
TSMC
Hsinchu, Fab12
TSMC
Tainan, Fab14
Global Foundries
40nm
eFlash
Dresden
Singapore
Backend Microcontroller
Frontend Microcontroller
Frontend
Silicon Foundry
QFP
BGA
Infineon
Backend
Backend Partner
AURIX
AURIX 2G
Dresden
Regensburg
Taiwan
South Korea
Malacca
Only C65nm
Only C65nm
C65nm QFP
C40nm QFP/BGA (dual Fab)
Only
C65nm
Bare die
Notes: BGA416 from AMKOR – should be ~50mpcs already (28mpcs out of 93mpcs total in late2012)

## Slide 12: Automotive Microcontroller AURIX™ Best-in-class supply chain security concept
Infineon provides a best-in-class supply chain security concept via TSMC for its next gen. microcontrollers
  2nd Fab Program: Products will be automatically transferred to the 2nd fab after crossing a certain volume threshold
  Emergency Bridging Program: Infineon plans to set up an additional emergency die bank stock to bridge a potential supply shortfall before the transfer of the products to the 2nd fab
Both fabs are regionally distributed and located on the safe west coast of Taiwan
Series production out of two fabs with same tool set
  1st and 2nd fab parts will be qualified for series production, OEM support provided
  In normal times: higher capacity flexibility by using both fabs for production
  In case of a line down: production from one fab can continue, no or limited efforts on customer side for requalification
TSMC Fab12
TSMC Fab14
2nd Fab
65nm
eFlash

## Slide 13: Infineon is committed to Zero Defect
Strong Development of ppm rate for MCU
Committed to Automotive Excellence
Infineon reached levels of below 1ppm for overall MCU portfolio as well as for leading edge 32bit controllers
Strong Zero Defect Program set up with Silicon Foundry partners to ensure high quality levels also for next generations
Notes: Application integration?
Voltage regulator?benefits?
13

## Slide 14: Table of contents
Infineon Microcontroller
1
  3
AURIX TC2xx PDH Support model
2
14
AURIX TC2xx Overview
3
  17
AURIX TC2xx Feature Details
4
  31
AURIX TC2xx Functional Safety
5
  51
AURIX TC2xx Security
6
  64
AURIX TC2xx Powertrain
7
  75
AURIX TC2xx xEV
8
  79
AURIX TC2xx CAV
9
  110
AURIX TC2xx Benchmarking vs. Competition
10
  118
AURIX TC2xx SW & Tools
11
  127

## Slide 15: Support Models: PDH Optimized open market AURIXTM and XMC™ customer support set up

## Slide 16: AURIX™ PDH partners Optimized regional and application specific presence

## Slide 17: Table of contents
Infineon Microcontroller
1
  3
AURIX TC2xx PDH Support model
2
  14
AURIX TC2xx Overview
3
17
AURIX TC2xx Feature Details
4
  31
AURIX TC2xx Functional Safety
5
  51
AURIX TC2xx Security
6
  64
AURIX TC2xx Powertrain
7
  75
AURIX TC2xx xEV
8
  79
AURIX TC2xx CAV
9
  110
AURIX TC2xx Benchmarking vs. Competition
10
  118
AURIX TC2xx SW & Tools
11
  127

## Slide 18: AURIX™ Product Naming
SA K – TC 2 7 5 T – 64 F 200 N
Infineon product identifier
TriCore
Architecture
Series
Package Class
Feature Package
Memory Size
Memory Type
Frequency
Feature packages
- Production Dev., No HSM
P Prod. Dev., HSM enabled
E Emulation Dev., no HSM
F Emulation Dev., HSM enabled
A ADAS enhanced, HSM enabled
X Feature ext., HSM enabled
C Customer specific
Brand
Device
Primary
Option
Secondary Option
Temperature range
Flash size code
8 0.5MB
16 1 MB
24 1.5 MB
32 2 MB
2.5 MB
64 4 MB
96 6 MB
128 8 MB
Special Type
Special Type Code
N CAN FD ISO frame
W LQFP 0.5mm pitch
F TQFP 0.4mm pitch
L BGA 1.0 mm pitch
S LFBGA 0.8mm pitch
Q Fusion Quad QFP 0.5 mm pitch
Core Architecture
Core Architecture
T Triple Core
D Dual Core
S Single Core
L Single Core with Lockstep
Temp. Range
K -40°C - +125°C
L -40°C - +150°C
Package Class
9 LFBGA-516
8 BGA-416
7 LFBGA-292
5 LQFP-176
4 L/TQFP-144
3 TQFP-100
2 TQFP-80
0 Bare Die
Notes: Temp. Range
B 0°C - +70 °C
K -40°C - +125 °C
L -40°C - >+125°C

## Slide 19: Same architecture with scalable feature-sets and pin-outs
9x Series up to 8MB |  |  |  |  |  |  | 
7x Series up to 4MB |  |  |  |  |  |  | 
6x Series up to 2.5MB |  |  |  |  |  |  | 
3x Series up to 2 MB |  |  |  |  |  |  | 
2x Series up to 1 MB |  |  |  |  |  |  | 
1x Series up to 512 kB |  |  |  |  |  |  | 
 | TQFP-80 | TQFP-100 | LQFP-144 TQFP-144 | LQFP-176 | LFBGA-292 | BGA-416 | LFBGA-516
TC298T
300 MHz
TC267D
200 MHz
TC265D
200 MHz
TC275T
200 MHz
TC297T TC297TA/X
300 MHz
TC234L TC234LA/X
200 MHz
TC277T
200 MHz
TC224L/S
133 MHz
TC264D
TC264DA
200 MHz
TC223L/S
133 MHz
TC222L/S
133 MHz
TC213L/S
133 MHz
TC212L/S
133 MHz
TC233L
200 MHz
TC214L/S
133 MHz
TC237L
TC237LA/X
200 MHz
TC299T
TC299TX
300 MHz
Pin superset
Pin compatible
Complete Portfolio with GTM!
Flash & RAM scalability
Single Core to Triple Core

## Slide 20: AURIX™ Family – CAN FD ISO11898-1 Support
4ch | 9x Series up to 8MB |  |  |  |  |  |  |  | 
4ch | 7x Series up to 4MB |  |  |  |  |  |  |  | 
4ch | 6x Series up to 2.5MB |  |  |  |  |  |  |  | 
4ch | 3x Series up to 2 MB |  |  |  |  |  |  |  | 
2ch | 2x Series up to 1 MB |  |  |  |  |  |  |  | 
2ch | 1x Series up to 512 kB |  |  |  |  |  |  |  | 
fixed CAN-FD channels | *) number of channels to be confirmed | TQFP-80 | TQFP-100 | LQFP-144 TQFP-144 | LQFP-176 | LFBGA-292 | BGA-416 | LFBGA-516 | 
TC298T
300 MHz
TC267D
200 MHz
TC265D
200 MHz
TC275T
200 MHz
TC297T TC297TA/X
300 MHz
TC234L TC234LA/X
200 MHz
TC277T
200 MHz
TC224L/S
133 MHz
TC264D
TC264DA
200 MHz
TC223L/S
133 MHz
TC222L/S
133 MHz
TC213L/S
133 MHz
TC212L/S
133 MHz
TC233L
200 MHz
TC214L/S
133 MHz
TC237L
TC237LA/X
200 MHz
TC299T
TC299TX
300 MHz
TC299T
TC299TX
300 MHz
TC299T
TC299TX
300 MHz
TC299T
TC299TX
300 MHz

## Slide 21: AURIX™ Emulation Device Support for powertrain applications
MCDS Multicore Debugging Support
Extended SRAM / Trace Memory
-40°C - +125°C temperature range
Engineering sample ES grade only
*TC234LF: no ISO 11898-1:2015 support
9x Series up to 2.5MB |  |  |  |  | 
7x Series up to 2 MB |  |  |  |  | 
6x Series up to 1 MB |  |  |  |  | 
3x Series up to 512 kB |  |  |  |  | 
 | LQFP-144 TQFP-144 | LQFP-176 | LFBGA-292 | BGA-416 | LFBGA-516
TC299TF
300 MHz
TC298TF
300 MHz
TC277TF
200 MHz
TC297TF
300 MHz
TC265DE
200 MHz
TC264DE
200 MHz
TC234LF*
200 MHz
TC275TF
200 MHz
Notes: Update 11/13: 4x series devices

## Slide 22: ED Feature-Sets
 | 9x ED | 7x ED | 6x ED | 3x ED
Calibration RAM | 2 MB | 1 MB | 512 KB | 512 KB
Debug & Measurement | MCDS | MCDS | MCDS | MCDS
Tool interface | DAP, 2&3 pins AURORA, JTAG | DAP, 2&3 pins AURORA, (JTAG *) | DAP, 2&3 pins AURORA | DAP, 2&3 pins JTAG
Package | LFBGA-516 BGA-416 LFBGA-292 | LFBGA-292 LQFP-176 | LQFP-144 LQFP-176 | LQFP-144
Highlights
Reuse PCB and housing of production ECU
ED has no special pins except stand-by power supply
“Long thin cable” requires just external LVDS transceivers
Best in class debugging with time aligned parallel trace
320 Mbit/s DAP (Device Access Port) I/F with just 3 pins
2,5 Gbit/s AURORA trace I/F
New high end automotive measurement (MCDS trace based) 10 – 30 MByte/s time stamped XCP DAQ data already with DAP
* only BGA

## Slide 23: AURIX™ scalable family - next generation µC From low cost to high performance chassis applications
9x Series up to 8MB |  |  |  |  |  |  | 
7x Series up to 4MB |  |  |  |  |  |  | 
6x Series up to 2.5MB |  |  |  |  |  |  | 
3x Series up to 2 MB |  |  |  |  |  |  | 
2x Series up to 1 MB |  |  |  |  |  |  | 
1x Series up to 512 kB |  |  |  |  |  |  | 
 | TQFP-80 | TQFP-100 | LQFP-144 TQFP-144 | LQFP-176 | LFBGA-292 | BGA-416 | LFBGA-516
System solution
AURIX Microcontroller
Pre-driver & MOSFETs
Power supply
TC298T
300 MHz
TC267D
200 MHz
TC265D
200 MHz
TC275T
200 MHz
TC297T TC297TA/X
300 MHz
TC234L TC234LA/X
200 MHz
TC277T
200 MHz
TC224L/S
133 MHz
TC264D
TC264DA
200 MHz
TC223L/S
133 MHz
TC222L/S
133 MHz
TC213L/S
133 MHz
TC212L/S
133 MHz
TC233L
200 MHz
TC214L/S
133 MHz
TC237L
TC237LA/X
200 MHz
TC299T
TC299TX
300 MHz
Electronic power steering
Standard ESC & ABS
Airbag
Domain control
Sensor fusion
Full feature ESC
Damping
MCU Scalability
Performance & Flash
Software compatibility
Pin-compatibility
Diverse timer architecture
Power Consumption
On-chip DC/DC high-efficiency power supply
Safety/Security
Concept
ISO26262 compliance
HW redundancy options
Hardware security support
Hardware security enabled
All devices available as Qualified Samples/PPAP

## Slide 24: AURIX™ scalable family - next generation µC From low cost to high performance chassis applications
9x Series up to 8MB |  |  |  |  |  |  | 
7x Series up to 4MB |  |  |  |  |  |  | 
6x Series up to 2.5MB |  |  |  |  |  |  | 
3x Series up to 2 MB |  |  |  |  |  |  | 
2x Series up to 1 MB |  |  |  |  |  |  | 
1x Series up to 512 kB |  |  |  |  |  |  | 
 | TQFP-80 | TQFP-100 | LQFP-144 TQFP-144 | LQFP-176 | LFBGA-292 | BGA-416 | LFBGA-516
Latest connectivity
6x CAN/CAN FD
Ethernet (AVB support)
FlexRay
TC298T
300 MHz
TC267D
200 MHz
TC265D
200 MHz
TC275T
200 MHz
TC297T 300 MHz
TC234S/L
200 MHz
TC277T
200 MHz
TC224L/S
133 MHz
TC264D
TC264DA
200 MHz
TC223L/S
133 MHz
TC222L/S
133 MHz
TC213L/S
133 MHz
TC212L/S
133 MHz
TC233S/L
200 MHz
TC214L/S
133 MHz
TC237S/L
200 MHz
TC299T
300 MHz
Lighting
Power operating systems
HVAC
Smart Junction Box
Full feature BCM
Full feature Gateway
Integrated BCM & Gateway
MCU Scalability
Performance & Flash
Software compatibility
Pin-compatibility
Diverse timer architecture
Power Consumption
On-chip DC/DC high-efficiency power supply
Safety/Security
Concept
ISO26262 compliance
HW redundancy options
Hardware security support
Hardware security enabled
All devices available as Qualified Samples/PPAP
BCM
Gateway
Truck
Full feature BCM
Full feature Gateway
Integrated BCM & Gateway

## Slide 25: One Family - scalable across application Most scalable 32-bit MCU portfolio on the market
SAFETY: Complete Solution for Safety up to ASIL-D
SECURITY: Integrated hardware support for Security

## Slide 26: AURIX™ scalable family - next generation µC From low cost to high performance chassis applications
9x Series up to 8MB |  |  |  |  |  |  |  | 
7x Series up to 4MB |  |  |  |  |  |  |  | 
6x Series up to 2.5MB |  |  |  |  |  |  |  | 
3x Series up to 2 MB |  |  |  |  |  |  |  | 
2x Series up to 1 MB |  |  |  |  |  |  |  | 
1x Series up to 512 kB |  |  |  |  |  |  |  | 
 | TQFP-80 | TQFP-100 | LQFP-144 TQFP-144 | LQFP-176 | LFBGA-292 | BGA-416 | LFBGA-516 | 
TC298T
300 MHz
TC267D
200 MHz
TC265D
200 MHz
TC275T
200 MHz
TC297T 300 MHz
TC234S/L
200 MHz
TC277T
200 MHz
TC224L/S
133 MHz
TC264D
TC264DA
200 MHz
TC223L/S
133 MHz
TC222L/S
133 MHz
TC213L/S
133 MHz
TC212L/S
133 MHz
TC233S/L
200 MHz
TC214L/S
133 MHz
TC237S/L
200 MHz
TC299T
300 MHz
Auxiliaries
Mid Range
ECU: 6 MPI, 4 GDI
TCU: ECAT 5 speed, AMT, CVT
Premium
ECU: 4+ Diesel, 6+ GDI, 8+ MPI
TCU: ECAT 8+ speed
TC270T
300 MHz
TC260D
300 MHz
High End
ECU: 4 Diesel, 4 GDI, 6 MPI
TCU: ECAT 7 speed, DCT

## Slide 27: AURIX™ Core Architectures from single core to triple core lockstep w/ clock delay
Core
Triple Core Lockstep
-
„T“ Marking
Checker Core
Core
Main bus
Core
Peripheral bus
Flash
Main bus
Flash
Main bus
Core
Peripheral bus
Flash
Lockstep
-
„L“ Marking
Single Core
-
„S“ Marking
Dual Core Lockstep
-
„D“ Marking
Main bus
Core
Peripheral bus
Flash
Checker Core
Checker Core
Core
Core
Peripheral bus
Checker Core *
* 2nd checker core only in TC27x

## Slide 28: Infineon AURIXTM Enhanced Communication peripherals
CAN Flexible Data
Increased data payload up to 64 bytes
Flexible data rate
  5MBit/sec point to point
  2MBit/sec network communication
AutoSAR 4.0.3 is currently integrating CAN FD into specification
First market implementation sampling today
Includes Classical CAN
Ethernet
IEEE 802.3-2002 for Ethernet MAC standard compatible module with support of IP, TCP/IP, UDP..
100 MBit
Real-time stamping support (IEEE 1588-2008) for clock synchronization
Automatic CRC checksum and padding support
Standard MII and RMII interfaces
Integrated DMA controllers
AVB Streaming Support - IEEE 1722, IEEE 1733
AutoSAR V4 features supported
High Speed Serial Link
Master for clock source selectable
Flexible baud rates 5/20/40/80/160/320Mbps
Full-duplex at independent speeds
5 signal interface
Internal or external termination
Remote Register Read/Write Access
Efficient Data Streaming
Interrupt Virtualization
CRC16 protection
Extensive error detection
Based on IEEE 1596.3 General Purpose Link

## Slide 29: CAN FD Improvements in Automotive
In-car communications
Up to 2MBit/sec data rate
CAN FD w/ 32 Byte payload assumed
Flash Programming
Up to 5MBit/sec data rate
CAN FD w/ 64 Byte payload assumed
125kBit/sec
250kBit/sec
500kBit/sec
Arbitration Phase
Arbitration Phase
1MBit/sec
5 MBit/sec
Arbitration and data phase
Arbitration and data phase
500kBit/sec
1MBit/sec
2MBit/sec
Factor 11
Factor 4
Notes:   Note: Up to 8MBaud covered by CAN FD in Automation specification CiA601
  Factor 4/11 shows the total improvement of data throughput (payload + higher date rate)

## Slide 30: AURIXTM Innovative Power Supply Lower Power Consumption and Cost
Low Power Consumption
Independent peripheral enable/disable
Independent core frequency for multicore variant
Lockstep can be disabled at start-up if not needed.
Current jump limited to 100mA/100us to optimize decoupling caps
Innovative Power Supply:
  Integrated switch cap DCDC on single core variants
  Benefits
  Single supply MCU
  Reduced BOM as no inductance and MOSFETS are required anymore
 | TC23/2xL (1-2MB) 130MHz | TC21xL (512kB) 100MHz
LDO with internal pass device | <90mA In safety operation | <75mA In safety operation
Switched Cap DCDC + 1 flying cap | <50mA In safety operation | <40mA In safety operation
FLASH
CPU
RAM
ADC
EVR
3V3
5V
3V3
Aurix 1G/2G
1V3
1V3
3V3
5V/3V3
Flying Cap
Colors refer to voltage domains

## Slide 31: Table of contents
Infineon Microcontroller
1
  3
AURIX TC2xx PDH Support model
2
  14
AURIX TC2xx Overview
3
  17
AURIX TC2xx Feature Details
4
31
AURIX TC2xx Functional Safety
5
  51
AURIX TC2xx Security
6
  64
AURIX TC2xx Powertrain
7
  75
AURIX TC2xx xEV
8
  79
AURIX TC2xx CAV
9
  110
AURIX TC2xx Benchmarking vs. Competition
10
  118
AURIX TC2xx SW & Tools
11
  127

## Slide 32: AURIX™ standard devices overview
Feature Set |  | 29x Series | 27x Series | 26x Series | 23x Series | 22x Series | 21x Series
TriCore | # Cores / Checker | 3 / 1 | 2 / 1 | 1 / 1 | - / - | - / - | - / -
1.6P | Frequency | 2x300 / 1x200 MHz | 200 MHz | 200 MHz | - | - | -
TriCore | # Cores / Checker | - / - | 1 / 1 | 1 / - | 1 / 1 | 1 / 1 (1 / 0) | 1 / 1 (1 / 0)
1.6E | Frequency | - | 200 MHz | 200 MHz | 200 MHz | 133 MHz | 133 MHz
Flash | Program Flash | 8 MB | 4 MB | 2.5 MB | 2 MB | 1 MB | 512 KB
 | EEPROM @ w/e cycles | 128 KB @ 500k | 64 KB @ 500k | 16 KB @ 500k | 128k @ 125 k cycles | 96k @ 125k cycles | 64k @ 125k cycles
SRAM | Total (DMI , PMI, LMU) | 728 KB | 472 KB | 240 KB | 192 KB | 96 KB | 56 KB
DMA | Channels | 128 | 64 | 48 | 16 | 16 | 16
ADC | Modules 12bit / DS | 11 / 10 | 8 / 6 | 4 / 3 | 2 / - | 2 / - | 2 / -
 | Channels 12bit / DS | 84 / 10 diff | 60 / 6 diff | 50 / 3 diff | 24 / - | 24 / - | 24 / -
Timer | GTM Input / Output | 48 / 152 channels | 32 / 88 channels | 24 / 64 channels | 8 / 32 | 8 / 32 | 8 / 32
 | CCU / GPT modules | 2 / 1 | 2 / 1 | 2 / 1 | 2 / 1 | 2 / 1 | 2 / 1
Interfaces | FlexRay (#/ch.) | 2 / 4 | 1 / 2 | 1 / 2 | 1 / 2 | - | -
 | CAN FD1) (nodes/obj) | 6 / 384 | 4 / 256 | 5 / 256 | 6 / 256 | 3 / 128 | 3 / 128
 | QSPI / ASCLIN / I2C | 6 / 4 / 2 | 4 / 4 / 1 | 4 / 4 / 1 | 4 / 2 / - | 4 / 2 / - | 4 / 2 / -
 | SENT / PSI5 / PSI5S | 15 / 5 / 1 | 10 / 3 / 1 | 6 / 2 / 1 | 4 / - | 4 / - | 4 / -
 | HSCT / MSC / EBU | 1 / 3 diff LVDS / 1 | 1 / 2 diff LVDS / - | 1 / 2 diff LVDS / - | - / - / - | - / - / - | - / - / -
 | Other | Ethernet | Ethernet | Ethernet | - | - | -
Safety | SIL Level | ASIL-D | ASIL-D | ASIL-D | ASIL-D | ASIL-D | ASIL-D
Security | HSM | Yes | Optional | No | Optional | No | No
Power | EVR | Yes | Yes | Yes | Yes | Yes | Yes
Option: CAN FD ISO ISO 11898-1 in 4/6, 4/5, 4/4, 3/3 nodes
Notes: Programm Flash vs Data Flash (EEProm emulated by data flash) 1k cyles vs. 125k
Pflash is faster (around 7 clocks) than Dflash (around 10 clocks )
SRI 300 MHz 64 bits breit
PRB max. 100 mhz

## Slide 33: 9x Series – Umbrella Device SAK-TC29xTP-128F300
Feature Set |  | 9x Series
TriCore 1.6P | # Cores / Checker | 3 / 1
 | Frequency 2) | 2x300 / 1x2002) MHz
Flash | Program Flash | 8 MB
 | EEProm @ w/e cycles | 128 KB @ 500k
SRAM | Total (DMI , PMI, LMU) | 728 KB
DMA | Channels | 128
ADC | Modules 12bit / DS | 11 / 10
 | Channels 12bit / DS | 84 / 10 diff
Timer | GTM Input / Output | 48 / 152 channels
 | CCU / GPT modules | 2 / 1
Interfaces | FlexRay (#/ch.) | 2 / 4
 | CAN FD3) (nodes/obj) | 6 / 384
 | QSPI / ASCLIN / I2C | 6 / 4 / 2
 | SENT / PSI5 / PSI5S | 15 / 5 / 1
 | HSCT / MSC / EBU | 1 / 3 diff LVDS / 1
 | Other | Ethernet MAC
Safety | SIL Level | ASIL-D
Security | HSM | Yes
Power | EVR | Yes
 | Standby Control Unit | Support
Package Variants
FCE
HSCT
SCU
DS-ADCx
ADCx
PLL &
PLL ERAY
FlexRay
MultiCAN+FD
QSPIx
ASCLINx
SENT
MSCx
STM
Ethernet
I²C
TriCore
1.6P
PMI
DMI Overlay
FPU
HSM
GTM
CCU6x
TriCore
1.6P
PMI
FPU
TriCore
1.6P
PMI
DMI Overlay
Standby
FPU
Checker Core
BCU
Ports
OCDS
GPT12x
IOM
System Peripheral Bus
PMU
Data Flash BROM HSM DFlash
Progr. Flash
Progr. Flash
Progr. Flash
Progr. Flash
RAM
LMU
EBU
SRI Cross Bar
LFBGA-516 0.8mm
-40°C to +125°C, 1) 84 ADC inputs
BGA-416 1.0mm
-40°C to +125°C 1)
60 ADC inputs
LFBGA-292 0.8mm -40°C to +125°C 1)
60 ADC inputs
DMI Overlay
Bare Die
Tjmax 170°C,
84 ADC inputs
EVR
5V or 3.3V single supply
SDMA
System Peripheral Bus
Bridge
PSI5(S)
Grade 0 option available on request with specific limitations for Ta=150°
High performance version with 3x300MHz on request with specific limitations
Option: CAN FD

## Slide 34: 7x Series – Umbrella Device SAK-TC27xTP-64F200
Feature Set |  | 7x Series
TriCore 1.6P | # Cores / Checker | 2 / 1
 | Frequency | 200 MHz
TriCore 1.6E | # Cores / Checker | 1 / 1
 | Frequency | 200 MHz
Flash | Program Flash | 4 MB
 | EEPROM @ w/e cycles | 64 KB @ 500k
SRAM | Total (DMI , PMI) | 472 KB
DMA | Channels | 64
ADC | Modules 12bit / DS | 8 / 6
 | Channels 12bit / DS | 60 / 6 diff
Timer | GTM Input / Output | 32 / 88 channels
 | CCU / GPT modules | 2 / 1
Interfaces | FlexRay (#/ch.) | 1 / 2
 | CAN-FD3) (nodes/obj) | 4 / 256
 | QSPI / ASCLIN / I2C | 4 / 4 / 1
 | SENT / PSI5 / PSI5S | 10 / 3 / 1
 | HSCT / MSC / EBU | 1 / 2 diff LVDS / -
 | Other | Ethernet MAC
Safety | SIL Level | ASIL-D
Security | HSM | Optional
Power | EVR | Yes
FCE
HSCT
SCU
DS-ADCx
ADCx
PLL &
PLL ERAY
FlexRay
MultiCAN+FD
QSPIx
ASCLINx
SENT
MSCx
STM
Ethernet
I²C
TriCore
1.6P
PMI
DMI Overlay
FPU
SRI Cross Bar
PSI5(S)
HSM
GTM
CCU6x
TriCore
1.6P
PMI
DMI Overlay
FPU
Checker Core
TriCore
1.6E
PMI
DMI Standby
Overlay
FPU
Checker Core 2)
BCU
Package Variants
Ports
OCDS
GPT12x
IOM
System Peripheral Bus
PMU
Data Flash BROM HSM DFlash
Progr. Flash
Progr. Flash
LFBGA-292 0.8mm
-40°C to +125°C 1)
60 ADC inputs
LQFP-176 0.5mm -40°C to +125°C 1)
48 ADC inputs
Bare Die Tjmax 170°C
60 ADC inputs
RAM
LMU
EVR
5V or 3.3V single supply
SDMA
System Peripheral Bus
Bridge
Grade 0 option available on request with specific limitations for Ta=150°
Option: CAN FD ISO ISO 11898-1 in all nodes

## Slide 35: 6x Series – Umbrella Device SAK-TC26xD-40F200
Feature Set |  | 6x Series
TriCore 1.6P | # Cores / Checker | 1 / 1
 | Frequency | 200 MHz
TriCore 1.6E | # Cores / Checker | 1 / -
 | Frequency | 200 MHz
Flash | Program Flash | 2.5 MB
 | EEPROM @ w/e cycles | 16 KB @ 500k
SRAM | Total (DMI , PMI) | 240 KB
DMA | Channels | 48
ADC | Modules 12bit / DS | 4 / 3
 | Channels 12bit / DS | 50 / 3 diff
Timer | GTM Input / Output | 24 / 64 channels
 | CCU / GPT modules | 2 / 1
Interfaces | FlexRay (#/ch.) | 1 / 2
 | CAN FD2) (nodes/obj) | 5 / 256
 | QSPI / ASCLIN / I2C | 4 / 4 / 1
 | SENT / PSI5 / PSI5S | 6 / 2 / 1
 | HSCT / MSC / EBU | 1 / 2 diff LVDS / -
 | Other | Ethernet MAC
Safety | SIL Level | ASIL-D
Security | HSM | No
Power | EVR | Yes
Package Variants
SDMA
FCE
HSCT
SCU
DS-ADCx
ADCx
PLL &
PLL ERAY
FlexRay
MultiCAN+FD
QSPIx
ASCLINx
SENT
MSCx
STM
Ethernet
I²C
SRI Cross Bar
GTM
TriCore
1.6P
PMI
DMI Overlay
FPU
Checker Core
TriCore
1.6E
PMI
DMI Standby
Overlay
FPU
BCU
Ports
OCDS
IOM
System Peripheral Bus
PMU
Data Flash BROM
Progr. Flash
EVR
5V or 3.3V
single supply
LQFP-176 0.5mm -40°C to +125°C 1)
50 ADC inputs
LQFP-144 0.5mm -40°C to +125°C 1)
40 ADC inputs
Bare Die Tjmax 170°C
50 ADC inputs
Bridge
PSI5(S)
CCU6x
GPT12x
LFBGA-292 0.8mm -40°C to +125°C 1)
50 ADC inputs
Grade 0 option available on request with specific limitations for Ta=150°
Option: Option: CAN FD ISO ISO 11898-1 in 4 nodes

## Slide 36: 3x Series – Umbrella Device SAK-TC23xLP-32F200
Feature Set |  | 3x Series
TriCore 1.6P | # Cores / Checker | - / -
 | Frequency | -
TriCore 1.6E | # Cores / Checker | 1 / 1
 | Frequency | 200 MHz
Flash | Program Flash | 2 MB
 | Data Flash | 128k , 125 k cycles
SRAM | Total (DMI, PMI) | 192 KB
DMA | Channels | 16
ADC | Modules 12bit / DS | 2 / -
 | Channels 12bit / DS | 24 / -
Timer | GTM Input / Output | 8 / 32
 | CCU / GPT modules | 2 / 1
Interfaces | FlexRay (#/ch.) | 1 / 2
 | CAN FD3) (nodes/obj) | 6 / 256
 | QSPI / ASCLIN / I2C | 4 / 2 / -
 | SENT / PSI5 | 4 / -
 | HSCT/ MSC / EBU | - / - / -
 | Other | -
Safety | SIL Level | ASIL-D
Security | HSM | Optional
Power | EVR | Yes
Package Variants
SCU
ADCx
PLL &
PLL ERAY
FlexRay
MultiCAN+FD
QSPIx
ASCLINx
SENT
STM
GTM
CCU6x
TriCore
1.6E
DMI Standby
Overlay
FPU
Checker Core
BCU
Ports
OCDS
GPT12x
IOM
System Peripheral Bus
EVR
3.3V
Single Supply
PMI
SDMA
TQFP-100
0.4mm -40°C to +125°C 1)
24 ADC inputs
TQFP-144
0.4mm -40°C to +125°C 1)
24 ADC inputs
PMU
Data Flash BROM
Progr. Flash
SRI Cross Bar
HSM
Bridge
LFBGA-292 0.8mm -40°C to +125°C 1)
24 ADC inputs
Grade 0 option available on request with specific limitations for Ta=150°
Option: CAN FD ISO ISO 11898-1 in 4 nodes
Notes: Updates
- Fußnoten aktualisiert

## Slide 37: 2x Series – Umbrella Device SAK-TC22xL(S)-16F133
Feature Set |  | 2x Series
TriCore 1.6P | # Cores / Checker | - / -
 | Frequency | -
TriCore 1.6E | # Cores / Checker | 1 / 1 (1 / 0)
 | Frequency | 133 MHz
Flash | Program Flash | 1 MB
 | Data Flash | 96k, 125k cycles
SRAM | Total (DMI, PMI) | 96 KB
DMA | Channels | 16
ADC | Modules 12bit / DS | 2 / -
 | Channels 12bit / DS | 24 / -
Timer | GTM Input / Output | 8 / 32
 | CCU / GPT modules | 2 / 1
Interfaces | FlexRay (#/ch.) | -
 | CAN FD2) (nodes/obj) | 3 / 128
 | QSPI / ASCLIN / I2C | 4 / 2 / -
 | SENT / PSI5 | 4 / -
 | HSCT/ MSC / EBU | - / - / -
 | Other | -
Safety | SIL Level | ASIL-D
Security | HSM | No
Power | EVR | Yes
Package Variants
SCU
ADCx
PLL
MultiCAN+FD
QSPIx
ASCLINx
SENT
STM
GTM
CCU6x
TriCore
1.6E
PMI
DMI Standby
Overlay
FPU
Checker Core
BCU
Ports
OCDS
GPT12x
IOM
System Peripheral Bus
EVR
3.3V
Single Supply
SDMA
TQFP-100
0.4mm -40°C to +125°C 1)
24 ADC inputs
TQFP-144
0.4mm -40°C to +125°C 1)
24 ADC inputs
PMU
Data Flash BROM
Progr. Flash
SRI Cross Bar
TQFP-80
0.4mm -40°C to +125°C
14 ADC inputs
Grade 0 option available on request with specific limitations for Ta=150°
Option: Option: CAN FD ISO ISO 11898-1 in all nodes
Notes: Updates
- Fußnoten aktualisiert

## Slide 38: 1x Series – Umbrella Device SAK-TC21xL(S)-8F133
Feature Set |  | 1x Series
TriCore 1.6P | # Cores / Checker | - / -
 | Frequency | -
TriCore 1.6E | # Cores / Checker | 1 / 1 (1 / 0)
 | Frequency | 133 MHz
Flash | Program Flash | 512 KB
 | Data Flash | 64k, 125k cycles
SRAM | Total (DMI , PMI) | 56 KB
DMA | Channels | 16
ADC | Modules 12bit / DS | 2 / -
 | Channels 12bit / DS | 24 / -
Timer | GTM Input / Output | 8 / 32
 | CCU / GPT modules | 2 / 1
Interfaces | FlexRay (#/ch.) | -
 | CAN FD2) (nodes/obj) | 3 / 128
 | QSPI / ASCLIN / I2C | 4 / 2 / -
 | SENT / PSI5 | 4 / -
 | HSCT/ MSC / EBU | - / - / -
 | Other | -
Safety | SIL Level | ASIL-D
Security | HSM | No
Power | EVR | Yes
Package Variants
SCU
ADCx
PLL
MultiCAN+FD
QSPIx
ASCLINx
STM
GTM
CCU6x
TriCore
1.6E
PMI
DMI Standby
Overlay
FPU
BCU
Ports
OCDS
GPT12x
IOM
System Peripheral Bus
EVR
3.3V
Single Supply
Checker Core
SDMA
SENT
PMU
Data Flash BROM
Progr. Flash
SRI Cross Bar
TQFP-100
0.4mm -40°C to +125°C 1)
24 ADC inputs
TQFP-144
0.4mm -40°C to +125°C 1)
24 ADC inputs
TQFP-80
0.4mm -40°C to +125°C
14 ADC inputs
Grade 0 option available on request with specific limitations for Ta=150°
Option: Option: CAN FD ISO ISO 11898-1 in all nodes
Notes: Updates
- Fußnoten aktualisiert

## Slide 39: AURIX™ special devices overview
Feature Set Special Devices |  | 29x Xtended | 29x ADAS | 26x ADAS | 23x Xtended | 23x ADAS
TriCore | # Cores / Checker | 3 / 1 | 3 / 1 | - / - | - / - | - / -
1.6P | Frequency | 2x300 / 1x200 MHz | 2x300 / 1x200 MHz | - | - | -
TriCore | # Cores / Checker | - / - | - / - | 1 / - | 1 / 1 | 1 / 1
1.6E | Frequency | - | - | 200 MHz | 200 MHz | 200 MHz
Flash | Program Flash | 8 MB | 8 MB | 2.5 MB | 2 MB | 2 MB
 | EEProm @ w/e cycles | 128 KB @ 500k | 128 KB @ 500k | 16 KB @ 500k | 128k , 125 k cycles | 128k , 125 k cycles
SRAM | Total (DMI , PMI, LMU) | 728 KB + 2MB | 728 KB + 2MB | 240 KB + 512 KB | 192 KB + 512KB | 192 KB + 512KB
DMA | Channels | 128 | 128 | 48 + ADAS DMA | 16 | 16
ADC | Modules 12bit / DS | 11 / 10 | 11 / 10 | 4 / 3 | 4/ - | 4 / -
 | Channels 12bit / DS | 84 / 10 diff | 84 / 10 diff | 40 / 3 diff | 24 / - | 24 / -
Timer | GTM Input / Output | 48 / 152 channels | 48 / 152 channels | 24 / 64 channels | 8 / 32 | 8 / 32
 | CCU / GPT modules | 2 / 1 | 2 / 1 | 2 / 1 | 2 / 1 | 2 / 1
Interfaces | FlexRay (#/ch.) | 2 / 4 | 2 / 4 | 1 / 2 | 1 / 2 | 1 / 2
 | CAN FD1) (nodes/obj) | 6 / 384 | 6 / 384 | 5 / 256 | 6 / 256 | 6 / 256
 | QSPI / ASCLIN / I2C | 6 / 4 / 2 | 6 / 4 / 2 | 4 / 4 / 1 | 4 / 2 / - | 4 / 2 / -
 | SENT / PSI5 / PSI5S | 15 / 5 / 1 | 15 / 5 / 1 | 6 / 2 / 1 | 4 / - | 4 / -
 | HSCT / MSC / EBU | 1 / 3 diff LVDS / 1 | 1 / 3 diff LVDS / 1 | 1 / 2 diff LVDS / - | - / - / - | - / - / -
 | Other | Ethernet | Ethernet, CIF, FFT accelerator | Ethernet, CIF, FFT accelerator | Ethernet | Ethernet, FFT accelerator
Safety | SIL Level | ASIL-D | ASIL-D | ASIL-D | ASIL-D | ASIL-D
Security | HSM | Yes | Optional | No | Option | Option
Power | EVR | Yes | Yes | Yes | Yes | Yes
Option: CAN FD ISO ISO 11898-1 in 4/6 fot TC29x, 4/5 nodes for TC26x, 0/6 nodes for TC23x

## Slide 40: 9x Series – feature eXtension SAK-TC299TX-128F300 / SAK-TC297TX-128F300
Feature Set |  | 9x Series
TriCore 1.6P | # Cores / Checker | 3 / 1
 | Frequency 2) | 2x300 / 1x200 MHz
Flash | Program Flash | 8 MB
 | EEProm @ w/e cycles | 128 KB @ 500k
SRAM | Total (DMI , PMI, LMU) | 728 KB + 2MB
DMA | Channels | 128
ADC | Modules 12bit / DS | 11 / 10
 | Channels 12bit / DS | 84 / 10 diff
Timer | GTM Input / Output | 48 / 152 channels
 | CCU / GPT modules | 2 / 1
Interfaces | FlexRay (#/ch.) | 2 / 4
 | CAN FD3) (nodes/obj) | 6 / 384
 | QSPI / ASCLIN / I2C | 6 / 4 / 2
 | SENT / PSI5 / PSI5S | 15 / 5 / 1
 | HSCT / MSC / EBU | 1 / 3 diff LVDS / 1
 | Other | Ethernet MAC
Safety | SIL Level | ASIL-D
Security | HSM | Yes
Power | EVR | Yes
Package Variants
FCE
HSCT
SCU
DS-ADCx
ADCx
PLL &
PLL ERAY
FlexRay
MultiCAN+FD
QSPIx
ASCLINx
SENT
MSCx
STM
Ethernet
I²C
TriCore
1.6P
PMI
DMI Overlay
FPU
HSM
GTM
CCU6x
TriCore
1.6P
PMI
FPU
TriCore
1.6P
PMI
DMI Overlay
Standby
FPU
Checker Core
BCU
Ports
OCDS
GPT12x
IOM
System Peripheral Bus
PMU
Data Flash BROM HSM DFlash
Progr. Flash
Progr. Flash
Progr. Flash
Progr. Flash
RAM
LMU
EBU
SRI Cross Bar
LFBGA-516 0.8mm
-40°C to +125°C, 1) 84 ADC inputs
DMI Overlay
EVR
5V or 3.3V single supply
SDMA
System Peripheral Bus
Bridge
PSI5(S)
HOT option available on request Ta>135°C
High performance version with 3x300MHz on request with specific limitations
Option: CAN FD ISO 11898-1 in 4 nodes
LFBGA-292
0.8mm -40°C to +125°C
60 ADC inputs

## Slide 41: 9x Series – ADAS Feature Set SAK-TC297TA-128F300
Feature Set |  | 9x Series
TriCore 1.6P | # Cores / Checker | 3 / 1
 | Frequency | 2x300 / 1x200 MHz
Flash | Program Flash | 8 MB
 | EEProm @ w/e cycles | 128 KB @ 500k
SRAM | Total (DMI , PMI, LMU) | 728 KB + 2MB
DMA | Channels | 128
ADC | Modules 12bit / DS | 11 / 10
 | Channels 12bit / DS | 84 / 10 diff
Timer | GTM Input / Output | 48 / 152 channels
 | CCU / GPT modules | 2 / 1
Interfaces | FlexRay (#/ch.) | 2 / 4
 | CAN FD2) (nodes/obj) | 6 / 384
 | QSPI / ASCLIN / I2C | 6 / 4 / 2
 | SENT / PSI5 / PSI5S | 15 / 5 / 1
 | HSCT / MSC / EBU | 1 / 3 diff LVDS / 1
 | Other | Ethernet MAC, CIF, FFT engine
Safety | SIL Level | ASIL-D
Security | HSM | Optional
Power | EVR | Yes
Package Variants
FCE
HSCT
SCU
DS-ADCx
ADCx
PLL &
PLL ERAY
FlexRay
MultiCAN+FD
QSPIx
ASCLINx
SENT
MSCx
STM
Ethernet
I²C
TriCore
1.6P
PMI
DMI Overlay
FPU
HSM
GTM
EVR
5V single supply
CCU6x
TriCore
1.6P
PMI
FPU
TriCore
1.6P
PMI
DMI Overlay
Standby
FPU
Checker Core
BCU
Ports
OCDS
GPT12x
IOM
System Peripheral Bus
EBU
LFBGA-292
0.8mm -40°C to +125°C
60 ADC inputs
DMI Overlay
RAM
M-JPEG/CIF
LMU
SRI Cross Bar
FFT engine
SDMA
System Peripheral Bus
Bridge
PSI5(S)
PMU
Data Flash BROM HSM DFlash
Progr. Flash
Progr. Flash
Progr. Flash
Progr. Flash
“High performance version with 3x300MHz on request with limited functionality”
Option: CAN FD ISO 11898-1 in 4 nodes

## Slide 42: 6x Series – ADAS Feature Set SAK-TC264DA-40F200
Feature Set |  | 6x Series
TriCore 1.6P | # Cores / Checker | 1 / 1
 | Frequency | 200 MHz
TriCore 1.6E | # Cores / Checker | 1 / -
 | Frequency | 200 MHz
Flash | Program Flash | 2.5 MB
 | EEProm @ w/e cycles | 16 KB @ 500k
SRAM | Total (DMI , PMI) | 240 KB + 512 KB
DMA | Channels | 48 + ADAS DMA
ADC | Modules 12bit / DS | 4 / 3
 | Channels 12bit / DS | 40 / 3 diff
Timer | GTM Input / Output | 24 / 64 channels
 | CCU / GPT modules | 2 / 1
Interfaces | FlexRay (#/ch.) | 1 / 2
 | CAN FD1) (nodes/obj) | 5 / 256
 | QSPI / ASCLIN / I2C | 4 / 4 / 1
 | SENT / PSI5 / PSI5S | 6 / 2 / 1
 | HSCT / MSC / EBU | 1 / 2 diff LVDS / -
 | Other | Ethernet MAC CIF, FFT accelerator
Safety | SIL Level | ASIL-D
Security | HSM | No
Power | EVR | Yes
Package Variants
LFQFP 144 0.5mm -40°C to +125°C
40 ADC inputs
HSCT
SCU
DS-ADCx
ADCx
PLL &
PLL ERAY
FlexRay
MultiCAN+FD
STM
Ethernet
GTM
CCU6x
TriCore
1.6P
PMI
DMI Standby
Overlay
FPU
Checker Core
TriCore
1.6E
PMI
DMI Standby
Overlay
FPU
BCU
Ports
OCDS
GPT12x
System Peripheral Bus
PMU
Data Flash BROM
Progr. Flash
SRI Cross Bar
FCE
QSPIx
I²C
IOM
ASCLINx
EVR
3.3V or 5V
single supply
RAM
M-JPEG/CIF
LMU
FFT engine
SDMA
Bridge
Option: CAN FD ISO 11898-1 in 4 nodes
SENT
MSCx
PSI5(S)

## Slide 43: 3x Series – ADAS Feature Set SAK-TC234LA-32F200
Feature Set |  | 3x Series
TriCore 1.6P | # Cores / Checker | - / -
 | Frequency | -
TriCore 1.6E | # Cores / Checker | 1 / 1
 | Frequency | 200 MHz
Flash | Program Flash | 2 MB
 | Data Flash | 128k , 125 k cycles
SRAM | Total (DMI, PMI) | 192 KB + 512KB
DMA | Channels | 16
ADC | Modules 12bit / DS | 4 / -
 | Channels 12bit / DS | 24 / -
Timer | GTM Input / Output | 8 / 32
 | CCU / GPT modules | 2 / 1
Interfaces | FlexRay (#/ch.) | 1 / 2
 | CAN FD1) (nodes/obj) | 6 / 256
 | QSPI / ASCLIN / I2C | 4 / 2 / -
 | SENT / PSI5 | 4 / -
 | HSCT/ MSC / EBU | - / - / -
 | Other | FFT accelerator, Ethernet
Safety | SIL Level | ASIL-D
Security | HSM | Option
Power | EVR | Yes
Package Variants
SCU
ADCx
PLL &
PLL ERAY
FlexRay
MultiCAN+FD
QSPIx
ASCLINx
SENT
STM
GTM
CCU6x
TriCore
1.6E
DMI Standby
Overlay
FPU
Checker Core
BCU
Ports
OCDS
GPT12x
IOM
System Peripheral Bus
EVR
3.3V
Single Supply
PMI
SDMA
TQFP-144
0.4mm -40°C to +125°C
24 ADC inputs
PMU
Data Flash BROM
Progr. Flash
SRI Cross Bar
RAM
LMU
FFT engine
HSM
Ethernet
Bridge
LFBGA-292
0.8mm -40°C to +125°C
24 ADC inputs
Option: CAN FD ISO 11898-1 in all nodes
SENT

## Slide 44: 3x Series – feature eXtension SAK-TC234LX-32F200
Feature Set |  | 3x Series
TriCore 1.6P | # Cores / Checker | - / -
 | Frequency | -
TriCore 1.6E | # Cores / Checker | 1 / 1
 | Frequency | 200 MHz
Flash | Program Flash | 2 MB
 | Data Flash | 128k , 125 k cycles
SRAM | Total (DMI, PMI) | 192 KB + 512KB
DMA | Channels | 16
ADC | Modules 12bit / DS | 4/ -
 | Channels 12bit / DS | 24 / -
Timer | GTM Input / Output | 8 / 32
 | CCU / GPT modules | 2 / 1
Interfaces | FlexRay (#/ch.) | 1 / 2
 | CAN (nodes/obj) | 6 / 256
 | QSPI / ASCLIN / I2C | 4 / 2 / -
 | SENT / PSI5 | 4 / -
 | HSCT/ MSC / EBU | - / - / -
 | Other | Ethernet
Safety | SIL Level | ASIL-D
Security | HSM | Option
Power | EVR | Yes
Package Variants
SCU
ADCx
PLL &
PLL ERAY
FlexRay
MultiCAN+FD
QSPIx
ASCLINx
SENT
STM
GTM
CCU6x
TriCore
1.6E
DMI Standby
Overlay
FPU
Checker Core
BCU
Ports
OCDS
GPT12x
IOM
System Peripheral Bus
EVR
3.3V
Single Supply
PMI
SDMA
TQFP-144
0.4mm -40°C to +125°C
24 ADC inputs
PMU
Data Flash BROM
Progr. Flash
SRI Cross Bar
RAM
LMU
HSM
Ethernet
Bridge
TQFP-144
0.4mm -40°C to +125°C
24 ADC inputs
SENT

## Slide 45: SRAM Configurations
Notes: Update 11/13: 4x SRAM increased
No separate Overlay SRAM – all available SRAM / EMEM / ext RAM can be used as overlay for Flash accesses
Standby RAM: DMI of Core 0
TC26x:2MB: 10,2% 2.5MB: 8,1%

## Slide 46: GTM Configurations and Scalability
GTM Versions
1.5.4-A3: TC27x B-Step, TC26x A-Step, TC29x A-Step
1.5.5-A1: TC27x C-Step, TC26x B-Step, TC29x B-Step
2.2.1: TC23x / TC22x
 |  | TC29x | TC27x | TC26x | TC23x / TC22x
Timer Inputs | Total channels | 48 | 32 | 24 | 8
TIM | 8 channels | 48 | 32 | 24 | 8
Timer Outputs | Total channels | 152 | 88 | 64 | 32
TOM | Standard 16-bit PWM ch. | 80 | 48 | 32 | 32
ATOM | Complex 24-bit PWM ch. | 72 | 40 | 32 | -
DTM | 2x4 ch | - | - | - | 2
SRAM | Total | 56,75 | 35,13 | 26,13 | -
MCS | Sequencer 1536x32bit | 36 | 24 | 18 | -
PSM | FIFO, 1024x29bit | 2 x 3,63 | 3,63 | 3,63 | -
DPLL | SRAM | 13,50 | 7,50 | 4,50 | -
Configuration |  |  |  |  | 
Clock Generation | DPLL | 1 | 1 | 1 | -
 | CMU | 1 | 1 | 1 | 1
 | TBU | 3 | 3 | 3 | 3
Processing | MCS | 6 | 4 | 3 | -
Pattern Evaluation | SPE | 4 | 2 | 2 | -
Broadcast Unit | BRC | 1 | 1 | 1 * | -
Safety | MON | 1 | 1 | 1 | -
 | CMP | 1 | 1 | 1 | -
* BLDC in B-step

## Slide 47: Flash Configuration
*1: maximum capability of the flash (stable 5V operation), achievable values depend on the interface bandwidth and SW overhead
*2: for Logical Size; w/e cycles for Physical Size: 125k

## Slide 48: ADC/DS Device Configurations
Table: SAR ADC configuration – as in final step of each device
 | 29x | 27x | 26x | 23x/22x/21x
 | 1 µs/ch | 1 µs/ch | 1 µs/ch | 1 µs/ch
Analog inputs [dedicated / overlaid with GPIO] | BGA516: 72/12 | BGA292: 48/12 | BGA292: 38/12 | BGA292: 24/0 QFP144: 24/0
 | BGA-416: 48/12 | QFP176: 36/12 | QFP176: 38/12 | QFP100: 24/0
 | BGA292: 48/12 |  | QFP144: 30/10 | QFP80: 14/0
Multiplexer Structure | 9 x 8 ch | 6 x 8 ch | 3x 16ch | 2x12 ch
 | 2 x 6 ch (overlaid) | 2 x 6 ch (overlaid) | 1x 12ch (overlaid) | 
12-bit SAR | 11 | 8 | 4 | 2
Delta-Sigma modules | 10x 1 diff ch | 6x 1 diff ch | 3x 1 diff ch | -
Multiplexer Granularity | 1x 4:1 (DS3) 4x 2:1 (DS2,DS6,DS7,DS8) 5x 1:1 (DS0,DS1,DS4, DS5,DS9) | 1x4:1 (DS3) 1x2:1 (DS2) 4x1:1 (DS0,DS1, DS4, DS5) | 1 x 4:1 (DS3) 1 x 2:1 (DS0) 1 x 1:1 (DS2) | -

## Slide 49: AURIX™ 5V single supply mode
 | 29x Series | 27x Series | 26x Series
Core | TriCore 1.6P | TriCore 1.6P/E | TriCore 1.6P/E
Frequency | 300 MHz | 200 MHz | 200 MHz
Concept | Triple Core with Lockstep | Triple Core with Lockstep | Dual Core with Lockstep
DC-DC / LDO | X | X | X
LDO ext PD | - | X | X
LDO int PD | - | - | Up to 133 MHz
 | EVR based single supply concept | External Components
DC-DC LDO | DC-DC regulator with an external switch device, diode and L+C for the 1.3V domain LDO with internal/external Pass Device for the 3.3V domain | DC-DC regulator (1.3V domain) Complementary Mosfet Inductor coil (3,3 - 6,8 uH) capacitor (10 - 22 uF)
LDO ext PD | LDO with an external Pass Device for the 1.3V domain LDO with internal Pass Device for 3.3V | LDO (1.3V domain) P-Ch. Mosfet
LDO int PD | LDO with internal Pass Device for both 1.3V and 3.3V domains. | 

## Slide 50: AURIX 3.3V single supply
 | EVR based single supply concept | External Components*
DC-DC | DC-DC regulator with an external switch device and L+C for the 1.3V domain | Complementary MOSFET Inductor coil (3,3 uH) Capacitor* (10 uF)
LDO ext PD | LDO with an external Pass Device for the 1.3V domain | P-Ch. MOSFET ; Capacitor* 1µF - 4.7µF
LDO int PD | LDO with internal Pass Device for 1.3V domain. | Capacitor* 1µF - 4.7µF
SC DCDC | switch cap DCDC regulator | Capacitors* 1 µ and 10µF - 22 µF
 | 29x Series | 27x Series | 26x Series | 23x, 22x, 21x Series
Core | TriCore 1.6P | TriCore 1.6P/E | TriCore 1.6P/E | TriCore 1.6E
Frequency | 300 MHz | 200 MHz | 200 MHz | 80-200MHz
Concept | Triple Core Lockstep | Triple Core Lockstep | Dual Core Lockstep | Single Core Lockstep
DC-DC / LDO | X | X | X | SC in 3x
LDO ext PD | - | X | X | -
LDO int PD | - | - | Up to 133 MHz | X
*not listed are additional decoupling Cs which are to be placed near to each supply pin for all voltages

## Slide 51: Table of contents
Infineon Microcontroller
1
  3
AURIX TC2xx PDH Support model
2
  14
AURIX TC2xx Overview
3
  17
AURIX TC2xx Feature Details
4
  31
AURIX TC2xx Functional Safety
5
51
AURIX TC2xx Security
6
  64
AURIX TC2xx Powertrain
7
  75
AURIX TC2xx xEV
8
  79
AURIX TC2xx CAV
9
  110
AURIX TC2xx Benchmarking vs. Competition
10
  118
AURIX TC2xx SW & Tools
11
  127

## Slide 52: Exemplary processing of a safety critical task
Sensor
Actuator
1
2
3
4
5
6
9
1
Analog to digital conversion
2
Sensor data pre-conditioning
3
Data transfer to SRAM
Fetching of data and/or code from flash
4
Data processing
5
6
Derived data transfer to timer
7
Timer data processing
8
Timer data transfer to communication interface
9
Communication to actuator
System
Micro-controller
Lockstep core domain
Lockstep cores support the safe processing of data, but many additional features are required to build a safe system!
GTM
7
8

## Slide 53: HW Integrity Testing Concept For detecting latent faults
System
Micro-controller
GTM
Safety IC
Check MCU
Correct?
Wait for
Answer
report
failure
yes
no
time out
Shut down of safety critical path and further appl. specific measures (as required)
Run
Tests
Question
Answer
Failure

## Slide 54: Diverse Lockstep CPU: Overview
Lockstep Architecture
  Physical Isolation
  Instruction-level execution Diversity
  Circuit-level Design & Timing Diversity
  Layout-level Diversity
  Avoid symmetries
Special design of clock & reset networks
Careful design of lockstep comparator
Infineon® Anti-Core the diverse lockstep concept

## Slide 55: IOM module (I/O monitoring) Real time signal comparison for error detection
Aurix IOM allows real time comparison
  PWM signals versus phase feedback
  HW support for multiple power stages
At EPS level
  Redundant and diverse and real time power stage monitors
    1 from TLE9180
    1 from AURIX
Customer benefits
  Real time comparison without CPU load as done using HW
  Power stage failure is detected earlier enabling optimized power stage design

## Slide 56: Development of IEC61508: relation to further safety standards
Agriculture  ISO 25119
Automotive  ISO 26262
Machinery  IEC 62061
Railway  EN 50129
Nuclear Power  IEC 61513
Process Industry  IEC 61511
Household Appliances  IEC 60335
Furnaces  IEC 50156
Aviation  DO-178
IEC 61508
Notes: (Schirmnorm/umbrella norm) Basis IEC 61508 für elektronische und elektrische systeme (E/E) im generellen das thema sicherheit definiert
Sehr allgemein gehalten geht nicht auf einzelne themen ein.
Davon abgeleitet die einzelnen safety standards

## Slide 57: Development of IEC61508: relation to further safety standards
Probability of Dangerouse Failure per Hour (PFHd) | SIL | SIL | PL | AgPL | ASIL
10e-9 | IEC 61508 | EN 62061 | EN ISO 13849 | ISO 25119 | ISO 26262
 | 4 | - | - | - | -
10e-8 |  |  |  |  | 
 | 3 | 3 | e | e | D
10e-7 |  |  |  |  | C
 | 2 | 2 | d | d | 
10e-6 |  |  |  |  | B
3x10e-6 | 1 | 1 | c | c | A
10e-5 |  |  | b | b | 
 | - | - | a | a | QM
1,00E-03 |  |  |  |  | 
 | - | - | - | QM | 
RISK
PL (Performance Level)
SIL (Safety Integrity Level)
Notes: (Schirmnorm/umbrella norm) Basis IEC 61508 für elektronische und elektrische systeme (E/E) im generellen das thema sicherheit definiert
Sehr allgemein gehalten geht nicht auf einzelne themen ein.
Davon abgeleitet die einzelnen safety standards

## Slide 58: AURIXTM –HW measures supporting safety
System
Micro-controller
B
A
A
A
A
A
Interrupt controller
Redundant, spatially separated peripherals
A
Bus Monitoring Unit
B
Safe DMA
C
C
Safe SRI
D
D
FLASH ECC (DECTED with enhancements to detect multi bit failures)
E
E
E
E
E
SRAM ECC (SECDED with enhancements to detect multi bit failures)
F
F
Lockstep core
G
G
Memory protection core
H
Memory protection peripherals
I
I
I
I
I
I
I
I
I
I
I
I
I
I
I
I
I
Safe Interrupt Processing
J
J
Flexible CRC Engine (FCE)
K
K
IO Monitor
L
L
Clock Monitoring
M
M
CPU self tests (90% Latent Fault Metric)
N
N
N
N
GTM
E
I
H
H
H
Notes: Message “AURIX safety architecture covers all safety relevant elements – much more than the lockstep CPU”
Dependability:=
OBD Feedback 7/10/14
- Passt. Evtl erweitern mit den Beispiel / Flussdiagramm

## Slide 59: AURIXTM Safety Implementation Concept
 | ASIL-C/D | ASIL-B | QM
Development Process Compliance |  |  | 
According to ISO26262 | Yes | Yes | No
HW Features |  |  | 
Lockstep core | Yes | No | No
Flash ECC | DECTED2, enhanced to support multi bit failures | DECTED2 | DECTED2
On-Line Flash ECC correction monitoring | Yes | No | No
SRAM ECC | SECDED1, enhanced to support multi bit failures | SECDED1 | SECDED1
SRAM Memory Monitor | Yes | No | No
Safe SRI | Yes | No | No
Safe DMA | Yes | Optional | No
FCE | Yes | Yes | No
IO Monitor | Yes | Optional | No
Safe Interrupt Processing | Yes | Yes | No
CPU Memory Protection | Yes | Yes | Yes
Peripheral Memory Protection | Yes | No | No
Bus Memory Protection | Yes | Yes | No
Clock Monitoring | Yes | Yes | No
Voltage Monitoring | Yes | Yes | No
HW CPU self tests | Latent fault metric 90% | N/A (SW test) | No
Redundant peripherals | SAR-ADC, QSPI, GTM, GPT12, CCU6 | No | No
SW Features |  |  | 
Cyclic SW Based Self test (SBST) | No | Yes Single Point Fault Metric 90% | No
Start up SW Based Self test (SBST) | Yes Latent fault metric 90% | Yes Latent fault metric 60% | No
Communication with external Watchdog | Yes | Yes | No
Runtime SRAM ECC Tests | Yes | Application level measures | No
Notes: SBST: SW Based Selftest
Single Point Fault Metric -> Safety goal is violated in every case
Latent Fault Metric -> Safety goal is violated in combination with 2nd fault

## Slide 60: Safety SW still needed - AURIXTM SafeTlib AURIXTM safety software available
Modular architecture:
  Test Handler
  SMU Driver
  MicroTest library
  SafeWDG stack
Reference code
  Test Manager
  SafeWDG Manager
  Start up sequence
  Integration in AUTOSAR environment including OS
Reduced customer effort
Reduce time-to market

## Slide 61: Safety Documentation and Support
One safety concept for the complete family
Best in class safety requirement tracking
Development in close cooperation with Exida and TÜV
AURIX is developed following ISO26262
AURIX is documented following ISO26262/IEC61508
  Safety Manual
  Safety Case
  FMEDA
Safety Application Guides
Safety Support
AURIX™ reduces efforts and helps to fulfil customer
safety needs

## Slide 62: IEC 61508 documentation AURIX™ for CAV and industrial safety applications
Safety documents:
FMEDA based on IEC61508
Safety manual which contains IEC61508 data
Safety Case:
Infineon will not provide the IEC61508 safety case, safety case will be based only on ISO26262
Safety case has to be done at the system level by the customer
Safety Support:
Will be handled by PDH and can be booked from customer directly at a PDH partner
Available now
Infineon Partners are published on:
www.infineon.com/pdh

## Slide 63: AURIX™ safety system architecture example EPS (electric power steering)
Sense
Compute
Actuate
Supply
Communicate
Rotor Position
iGMR Sensor
TLE 5009/12
Torque Sensor
TLE 4998
32-bit Lockstep MCU
AURIX™
TC233L
CAN Transceiver
TLE 6251D / TLE7250G
FlexRay
Transceiver (opt.)
VMCU
VSens
VLogic
VTx
3-Phase
Driver IC
TLE
9180
Motor Current
М
OptiMOS™-T2 40V
7x IPB180N04S4-01
VBAT
VBAT
TLF35584 Safety Power Supply
Failure Protection
Failure Diagnosis
Redundancy
Diverse Implementation

## Slide 64: Table of contents
Infineon Microcontroller
1
  3
AURIX TC2xx PDH Support model
2
  14
AURIX TC2xx Overview
3
  17
AURIX TC2xx Feature Details
4
  31
AURIX TC2xx Functional Safety
5
  51
AURIX TC2xx Security
6
64
AURIX TC2xx Powertrain
7
  75
AURIX TC2xx xEV
8
  79
AURIX TC2xx CAV
9
  110
AURIX TC2xx Benchmarking vs. Competition
10
  118
AURIX TC2xx SW & Tools
11
  127

## Slide 65: Car Security
ATTACKER
Unwanted access denied
Prioritization of Emergency Services
Toll Control
Traffic Jam Detection Accident Avoidance
Remote Diagnostics
Software Update
Car Repair Shop
eCall
Payment Systems
CAR2CLOUD
Infotainment
Traffic Information
Apps
ONBOARD Safety & security
CONSUMER DEVICE INTEGRATION
CAR2CAR
CAR2INFRASTRUCTURE
Internet Services

## Slide 66: Security Standard Compliance IFX Microcontroller Security Roadmap
SHE v1.1 TC1791/93/98
90 nm
65 nm
Med. EVITA HSM TC27x/TC29x TC23x
Full EVITA HSM
TC3xx
SHA-256 HW Hash Engine
ECC-256 HW
40 nm
Hardware
Software
SHE+ Emulation
access feasible via
CSM Integration
SHE+ Emulation
RSA/ECC Crypto Lib
In Production
In development
>SOP2011
>SOP2016
>SOP2018
AUDO MAXTM
AURIXTM
TC2xx
AURIXTM
TC3xx
In Production
Notes: Text and Story Telling
IFX ATV MC – Security Roadmap
MC will support the following automotive Security Generations
1.) legacy SHE with TC179x (AUDO MAX) for Design in Phases from SOP2011-2013
2.) medium EVITA specification with full 2/4/8MB derivative portfolio supporting HSM AURIX 65nm Generation beyond SOP 2014
3.) full EVITA (including HW accelerators for RSA1028 and ECC256) for the next 40nm technology µC node AURIX PLUS beyond SOP 2018
please further note, that IFX ATV MC is committed also to enable backwards compatibility to SHE by offering the HSM SHE emulation starting in the AURIX generation in 2015

## Slide 67: Security Standard Compliance IFX Microcontroller Security Roadmap
SHE v1.1 TC1791/93/98
90 nm
65 nm
Med. EVITA HSM TC23x/TC27x/TC29x
Full EVITA HSM
TC3xx –all devices
Hash Module
PKC Module
40 nm
Hardware
Software
SHE+ Emulation
access feasible via
CSM Integration
SHE+ Emulation
RSA/ECC Crypto Lib
In Production
In Development
>SOP2011
>SOP2015
>SOP2019
AUDO
MAXTM
AURIXTM
AURIXTM 2G
HSM 1stgeneration
A highly flexible and programmable solution in addition to SHE
Asymmetric crypto agility by software
Broadly supported within the AURIX™ MCU portfolio
HSM 2nd generation
  Hardware accelerators for 30 times more performance
  Asymmetric crypto agility by hardware
  Supported by all Infineon AURIX™ 2G variants
Secure Hardware Extention
Not Programmable
No asymmetric cryptography
Especific support within the AURIX™ MCU portfolio
In Production
Notes: Text and Story Telling
IFX ATV MC – Security Roadmap
MC will support the following automotive Security Generations
1.) legacy SHE with TC179x (AUDO MAX) for Design in Phases from SOP2011-2013
2.) medium EVITA specification with full 2/4/8MB derivative portfolio supporting HSM AURIX 65nm Generation beyond SOP 2014
3.) full EVITA (including HW accelerators for RSA1028 and ECC256) for the next 40nm technology µC node AURIX PLUS beyond SOP 2018
please further note, that IFX ATV MC is committed also to enable backwards compatibility to SHE by offering the HSM SHE emulation starting in the AURIX generation in 2015

## Slide 68: Performance Hardware Security Module (HSM) AURIXTM TC3xx: Full compliant
Flash
Peripherals
TriCore0
TriCore1
SRAM
Bridge
Firewall
32-bit CPU
SRAM
TRNG
PKC
ECC 256
Boot ROM
AES 128
HASH
SHA 2
Timer
HSM Domain
Peripherals
Peripherals
Trusted Execution
Environment
HSM Features
Performance & Flash
Pin-compatibility
32-bit processor with up to 100MHz CPU speed
  MPU (Memory Protection Unit)
  64KB SRAM
Flash
  Code storage in 4x64KB+2x16KB reserved HSM PFlash below 2MB
  Key Storage, Secure Data and Counter in HSM only 2x32kB Dflash
AES-128 Hardware Accelerator for symmetric block ciphers (5 contexts)
  ECB, CBC, CTR, OFB, CFB, GCM & XTS
True Random Number Generator (TRNG) to generate 128-bit random numbers
  AIS 31 class P2 compliant
PKC - ECC-256 Hardware Accelerator
SHA224/256 Hardware Accelerator

## Slide 69: AURIX™ Hardware Security Module A consequent security enhancement
Hardware Security Module (HSM)
A highly flexible and programmable solution
AES128 HW accelerator matching performance for automotive protocols
Crypto- and Algorithm Agility by Software
AIS31 compliant True Random Number Generator (TRNG) with high Random Entropie over Lifetime
Secure Platform
HSM: 32 bit CPU
AES Accelerator
Notes: Text and Story Telling
Secure Platform
as explained before, the HSM offers a 'trusted Execution Environment' which can host pure OEM owned Security SW.
this makes it beneficial to host on the one hand side OEM dedicated Security Applications (as an OEM differentiator), and on the other hand side prevents the unattended occurrence of malware or viruses
The AURIX Benefit in that context is, that this HSM SW can be completely encapsulated on dedicated protected FLASH resources.
In this way, the TriCore Application SW will have no chance to jeopardize the authenticity of the HSM original OEM HSM SW.

## Slide 70
Performance Hardware Security Module (HSM)
AURIXTM vs. AURIXTM 2G feature set overview
Performance HSM Features:
32-bit processor with up to 100MHz CPU speed
  MPU (Memory Protection Unit)
  64KB SRAM Flash
  Code storage in 4x64KB+2x16KB reserved HSM PFlash below 2MB
  Key Storage, Secure Data and Counter in HSM only 2x32kB DFlash
AES-128 Hardware Accelerator for symmetric block ciphers (5 contexts)
  ECB, CBC, CTR, OFB, CFB, GCM & XTS
PKC - ECC-256 Hardware Accelerator
    ≤ 100 ver/s or 200 sig/s
SHA224/256 Hardware Accelerator
  ≤ 2µs latency for 512 bit block (or ≈ ≤ 30MByte/s)
True Random Number Generator (TRNG) to generate 128-bit random numbers
  AIS 31 class P2 compliant
Delta Description AURIX versus AURIX 2G
  1x16KB/2x64KB versus 18x16KB (288KB) PFlash
  24KB/40KB versus 24KB/64KB SRAM
  no PKC HW accelerator versus PKC ECC256
  no SHA HW accelerator versus SHA 224/256

## Slide 71: IFX offering: AURIXTM HSM SHE + Emulation Mapping to Telematics use case
Typical applications | Tuning Protection | Immobilizer Secure-on-board communication | Possible extensions, depending on specific Tier1 / OEM use case
Key Management | √ | √ | √
Symmetric Data Encryption / Decryption | √ | √ | √
MAC Generation / Verification | √ | √ | √
Safe MAC Verification |  | √ | √
Random Number Management | √ | √ | √
Secure Boot | √ | √ | √
Debug Access | √ | √ | √
Other SHE Services | √ | √ | √
Asymmetric Encryption / Decryption | √ | √ | √

## Slide 72: AURIXTM HSM LLD Low Level Driver
HSM MCAL driver: read/write flags and status in HSM bridge (32 bit register) on TriCore side
    Configure interrupts for the flags (HSM  TriCore)
Bridge driver: Read/write flags and status in HSM bridge (32 bit register) on HSM side
    Configure interrupts (TriCore  HSM, from flags + external interrupts)
Crypto driver: Load / unload into AES, Encrypting and decrypting data, TRNG driver
HSM specific Flash EEPROM Emulation (FEE) + Flash (FLS) driver
Lib: cache handling (init, pre-fetch, write cache data to memory)
Notes: FEE: Flash EEPROM Emulation
FLS: Flash Treiber

## Slide 73: Infineon SHE+ Driver Software Architecture
CRY+: software interface abstracting the SHE+ features
HSMCom – HostCom: handles communication between TriCore and HSM
SHE+ Emulation Control: handles and process the CRY+ request coming from TriCore

## Slide 74: SHE+ Driver: Feature Overview
Main Features | Description
SHE Encryption / Decryption | Symmetrical 128 bit AES with cipher modes ECB and CBC
SHE CMAC | Symmetrical 128 bit AES Message Authentication Code
SHE CMAC including safe CMAC verify | Support a safe CMAC verification enabling the application to check the integrity of safety related data.
SHE load Plain Key | Store a 128bit key in HSM RAM. No security protocol involved.
SHE Export Key | Export the RAM key in a wrapped format. (encrypted and authenticated)
SHE load Key | Store a 128nit key in HSM non-volatile memory using a secure protocol.
SHE RNG | Generate pseudo-random value using AES. The seed is generated by a TRNG.
SHE secure boot | Verify the CMAC of the application start up code.
SHE Debug | Enable access to HSM debug interface using a secure protocol.
SHE Status | Get status of SHE.
SHE Cancel | Cancel the currently performed operation.
Error reporting | Report SHE error through an AUTOSAR mechanism additionally to CSM return code.
Timeout handling | Report an error if HSM response time is above a predefined limit.
Support during software update (cipher and MAC) | The cipher and MAC feature can be used also during update of the application software
TRNG | Support the generation of True Random Number Generation
Encryption OFB, CFB, CTR, XTS, GCM | Support additional AES modes
Key storage extension | Extend the non-volatile storage to more than 10 keys.

## Slide 75: Table of contents
Infineon Microcontroller
1
  3
AURIX TC2xx PDH Support model
2
  14
AURIX TC2xx Overview
3
  17
AURIX TC2xx Feature Details
4
  31
AURIX TC2xx Functional Safety
5
  51
AURIX TC2xx Security
6
  64
AURIX TC2xx Powertrain
7
75
AURIX TC2xx xEV
8
  79
AURIX TC2xx CAV
9
  110
AURIX TC2xx Benchmarking vs. Competition
10
  118
AURIX TC2xx SW & Tools
11
  127

## Slide 76: AURIX™ Powertrain solution key competence out of one hand (Gasoline Direct Injection)
System Benefits
Flexible and scalable product portfolio tailored to the performance and real-time needs of the premium and value segment
Conforming with the latest emission legislation at the highest possible fuel efficiency and maximum fun to drive
Benchmark-setting real-time performance facilitates down-sizing, direct injection, turbo charging and highly-efficient after-treatment
New sensor families provide enhanced measurement precision (e.g. ignition control, misfire detection)
32-bit
Multicore/Lockstep
MCU
AURIX™
e.g. TC27xT
4MB / 200 MHz
60x
SAR
SENT
GTM
4x
QSPI
E-Ray
4x
CAN
ASCLIN
2x
MSC
6x DS
HSM
HSSL
Ethernet
PSI5
Pedal Position
TLE4997/98
EGR-Throttle Position
TLE4997/98
Fuel Level
TLE4997/98
Swirl/Tumble Flap
TLE4997/98
Throttle Position
TLE4998S
Temperature
Sensor(s)
Barometric Pressure
KP23x, KP25x
Knock Sensor(s)
In-Cylinder Pressure
Sensors
Crankshaft
TLE502x/492x
Lambda Sensor
Camshaft
TLE4986
CAN
TLE7250G
FlexRay
TLE9221SX
LIN
TLE7259-3GE
…
…
2Ch.
5V/0.15A
5V/0.15A
5V/0.15A
3.3V or 5V/10mA
3.3V or 5V/0.6A
5V/0.2A
Battery (KL30)
Key (KL15)
Safety System Supply
Tracker 1
Tracker 2
Safe State
Controller
TLF35584
Window/Q&A-
Watchdog
StBy-
LDO
µC-LDO
Ref-LDO
Com-LDO
Engine Management
Typical Partitioning for GDI Discrete & Solenoid
Low-Side Ignition
Ignition Plugs
4x
15A pk.
GDI Driver
OptiMOS™
IPG20N10S4L-35A
IPD20N06S4L-14
H-Bridge for Throttle
TLE8209-2SA
H-Bridge for EGR
TLE9201SG
LS-Switch Flex
PWM, Current-Sense
Flex02
TLE8102SG
LS-Switch Flex8
On-Off Outputs
TLE8108EM
LS-Switch Flex
PWM Outputs
Flex18
TLE8718SA
4x
3/10A
Solenoid
Injectors
8A Ch.
5A Ch.
(eGas) Throttle
EGR Throttle
O2
2x 5/9A
8x 0.5A
4x 2.6A
2x 2.6A
4x 1.7A
2x 1A
Relays
Solenoid
VVT
Solenoid
Relais
MIL
UV/OV/Error-Monitoring
Powertrain CAN
General Purpose
H-Bridge
TLE9201SG
Turbo Charger
Waste Gate
5A Ch.
Manifold Air Pressure
KP21x, KP22x, KP27x*
Notes: Energy Efficiency for Combustion Engine Vehicles (from brochure)
Electronic automotive components are key to raising fuel efficiency levels and cutting emissions. The latest environment protection agency standards – Euro 5 and Euro 6 for passenger cars and Euro 3 and Euro 4 for motorcycles – are driving developments in advanced engine management. TriCore™-based products can be found in improved combustion technologies such as Homogeneous Charge Compression Ignition (HCCI) as well as in direct injection, smart turbocharger and valve actuation applications. They are also ideal for a range of innovative transmission technologies such as Double Clutch Transmission (DCT) and modern Continuous Variable Transmission (CVT).

## Slide 77: AURIXTM Powertrain solution key competence out of one hand (Diesel Direct Injection)
System Benefits
Large and scalable product portfolio tailored to the performance needs of the entire diesel segment
Meeting upcoming emission legislation at maximum fuel efficiency with the highest driving pleasure 
Benchmark-setting real-time performance facilitates in-cylinder pressure measurement and highly-efficient after-treatment (incl. hot and cold EGR, oxidation catalyst, particulate treatment, NOx treatment)
New sensor families provide enhanced measurement precision
Safety System Supply
Battery (KL30)
Key (KL15)
Engine Management
Typical Partitioning for DDI Discrete
32-bit
Multicore/Lockstep
MCU
AURIX™
e.g. TC29xT
8MB / 300 MHz
84x
SAR
SENT
GTM
6x
QSPI
2x
E-Ray
6x
CAN
ASCLIN
10x DS
HSM
HSSL
Ethernet
PSI5
Tracker 1
Tracker 2
Safe State
Controller
TLF35584
Window/Q&A-
Watchdog
StBy-
LDO
µC-LDO
Ref-LDO
Com-LDO
5V/0.15A
5V/0.15A
5V/0.15A
3.3V or 5V/10mA
3.3V or 5V/0.6A
5V/0.2A
Pedal Position
TLE4997/98
EGR-ThrottlTLE4997/98
e Position
Fuel Level
TLE4997/98
Swirl/Tumble Flap
TLE4997/98
Throttle Position
TLE4998S
Temperature
Sensor(s)
Barometric Pressure
KP23x, KP25x
Knock Sensor(s)
In-Cylinder Pressure
Sensors
Lambda Sensor
Crankshaft
TLE502x/492x
Camshaft
TLE4986
Powertrain CAN
…
…
CAN
TLE7250G
FlexRay
TLE9221SX
LIN
TLE7259-3GE
2Ch.
LS-Switch Flex
PWM Outputs
Flex18
TLE8718SA
LS-Switch Flex
PWM, Current-Sense
Flex02
TLE8102SG
LS-Switch Flex8
On-Off Outputs
TLE8108EM
H-Bridge for Throttle
TLE8209-2SA
H-Bridge for EGR
TLE9201SG
PROFET™
BTS500x0-1EGA
BTS500x0-1TMA/B
BTS500x0-1TEA/B
FAST IGBT
e.g. IHD04N60RA/
IDH06N60RA
6x 8A
6x 8A
8A Ch.
5A Ch.
2x 5/9A
4x 0.5A
4x 2.6A
2x 2.6A
4x 1.7A
2x 1A
Relays
MIL
Lamp
Solenoid
VVT
Solenoids
Relays
O2
EGR Throttle
(eGas) Throttle
Piezo Injectors
Glow Plugs
UV/OV/Error-Monitoring
General Purpose
H-Bridge
TLE9201SG
Turbo Charger
Waste Gate
5A Ch.
Manifold Air Pressure
KP21x, KP22x, KP27x*
3x
MSB
Notes: Energy Efficiency for Combustion Engine Vehicles (from brochure)
Electronic automotive components are key to raising fuel efficiency levels and cutting emissions. The latest environment protection agency standards – Euro 5 and Euro 6 for passenger cars and Euro 3 and Euro 4 for motorcycles – are driving developments in advanced engine management. TriCore™-based products can be found in improved combustion technologies such as Homogeneous Charge Compression Ignition (HCCI) as well as in direct injection, smart turbocharger and valve actuation applications. They are also ideal for a range of innovative transmission technologies such as Double Clutch Transmission (DCT) and modern Continuous Variable Transmission (CVT).

## Slide 78: Dry Double Clutch Transmission Electrical Control
32-bit
Multicore/Lockstep
MCU
AURIX™
e.g. TC27xT
4MB / 200 MHz
60x
SAR
SENT
GTM
4x
QSPI
E-Ray
4x
CAN
ASCLIN
2x
MSB
6x DS
HSM
HSSL
Ethernet
PSI5
Safety System Supply
Tracker 1
Tracker 2
Safe State
Controller
TLF35584
Window/Q&A-
Watchdog
StBy-
LDO
µC-LDO
Ref-LDO
Com-LDO
Battery (KL30)
Key (KL15)
5V/0.15A
5V/0.15A
5V/0.15A
3.3V or 5V/10mA
3.3V or 5V/0.6A
5V/0.2A
PRNDL Switches
TLE4964
Shift Position Sensor
TLE4997/98/6x
Temperature
Sensor
Rotor Position
iGMR Sensor
TLE5012B
FlexRay
TLE9221SX
CAN
TLE7250G
LIN
TLE7259-3GE
TLE9250SJ1)
Powertrain
FlexRay
Diagnostic/Instrumentation CAN
Diagnostic/
Instrumentation
3-Phase
Driver IC
TLE9180
3-Phase
Driver IC
TLE9180
3-Phase
Driver IC
TLE9180
3-Phase
Driver IC
TLE9180
Battery (KL30)
Key (KL15)
1st
Clutch
M
M
M
M
Rotor Position
iGMR Sensor
TLE5012B
Rotor Position
iGMR Sensor
TLE5012B
Rotor Position
iGMR Sensor
TLE5012B
Rotor Position
iGMR Sensor
TLE5012B
2nd
Clutch
Even
Gears
Odd
Gears
OptiMOS™-T2 40V
24x IPD90N04S4-04
1) In development
7-Speed Double Clutch Transmission
Typical Partitioning for Constant Current Control
UV/OV/Error-Monitoring
Output Shaft Speed
TLE4951/53/54
Output Shaft Speed
TLE4951/53/54
Output Shaft Speed
TLE4951/53/54
Input Shaft Speed
TLE4951/53/54
System Benefits
Full range of products ranging from voltage regulators, transceivers, sensors, microcontrollers and smart power drivers
Leading-edge OptiMOS™-T2 MOSFET technology combined with a robust package to deliver best-in-class performance and outstanding current capacity
Optimized sensors providing enhanced disturbance immunity (e.g. vibration) and direction detection
Reduces fuel consumption compared to manual transmission
Coherent chip-set solution for an easy and effective ISO26262 compliant system implementation

## Slide 79: Table of contents
Infineon Microcontroller
1
  3
AURIX TC2xx PDH Support model
2
  14
AURIX TC2xx Overview
3
  17
AURIX TC2xx Feature Details
4
  31
AURIX TC2xx Functional Safety
5
  51
AURIX TC2xx Security
6
  64
AURIX TC2xx Powertrain
7
  75
AURIX TC2xx xEV
8
79
AURIX TC2xx CAV
9
  110
AURIX TC2xx Benchmarking vs. Competition
10
  118
AURIX TC2xx SW & Tools
11
  127

## Slide 80: E-mobility: AURIXTM is an essential part of electrification, driving every e-application
Main Inverter
The inverter not only drives the electric motor, but is also used for regenerative braking and feeding energy back to the battery.
DC/DC Converter
The DC/DC converter charges the conventional 12 V power supply net from the high-voltage battery and replaces the former belt driven alternator.
Auxiliary Inverters/Converters
Instead of being belt-driven, auxiliaries like water pump, HVAC Compressor, PTC Heater, etc. also have to be driven by electric power. Inverters are needed to drive them smart and energy-efficient.
Battery Management
The battery management system controls battery state during charging and discharging. Intelligent functionality is needed to extend the battery lifetime, which has a considerable impact on the total cost of ownership. The State of Health (SoH), State of Charge (SoC) and Depth of Discharge (DoD) of the battery is permanently monitored.
On-board Charger
The battery block is charged via an AC/DC converter module. In the example shown here, an on-board unit charges the battery. Off-board and inductive charging solutions are also available.
HCU & Domain
In case of a hybrid car, Hybrid Control Unit or Vehicle Control Unit handle the inter-communication between sub-modules e.g. engine & hybrid motors inside a Hybrid EV. It can also serve as central gateway for Powertrain domain in the E/E architecture to ensure security communication between other domains.
AURIXTM for Main Inverter
Performs torque management & rotor positioning for efficient motor control
AURIXTM for DC/DC Converter
Handles the communication to AUTOSAR stack as well as execute control loops for multiple phases (up to 8)
AURIXTM for Auxiliary Inverters/Converters
Drives water pump, HVAC Compressor, PTC Heater as well as thermal management for more efficient energy use
AURIXTM for Battery Management
Monitors and reacts on State of Health (SoH), State of Charge(SoC) and Depth of Discharge (DoD) with the assistance of balancing ASICs; It prevents illegal manipulation both on system & battery packs via encrypted data-flow; It monitors system safety through SPI enabled ring topology.
AURIXTM for On-board Charger
Ensures galvanic insulation between mains and HV-battery,
As well as secure charge-billing, enables various power classes for flexible charging times
AURIXTM for HCU & Domain Control
handle the inter-communication between sub-modules e.g. engine & hybrid motors inside a Hybrid EV. Ensure secure communication & Software Over the Air(SOTA) as central gateway for Powertrain domain in the E/E architecture

## Slide 81: (H)EV: Infineon MCU inside AURIXTM driving every E-mobility application!
Inverter/HCU |  | DC-DC/OBC |  | BMS | 
 | VW MEB platform TC275 |  | Hyundai 48V Tucson TC264 |  | Daimler S Class 48V TC277
 | Ford C-Max & F150 TC298 |  | Mazda Atenza TC264 |  | Kia Soul TC264
 | Mercedes E Class TC277 |  | London Taxi Company TC265 & TC233 |  | Hyundai Sonata TC264
 | Suzuki Ertiga TC233 |  | AUDI E-Tron TC277 |  | BMW 530 TC277
 | AUDI Q5 HEV TC277 |  | SAIC Baojun730 TC275 |  | Next EV Nio TC275
 | Renault Twizy & Zoe TC1782 |  | Hyundai Avante XC164 |  | BJEV EU260 TC1782
 | Volvo XC90 TC1798 |  | VW Blue e-Motion TC1797 |  | AUDI A3 TC1797
 | BMW i3 & i8 TC1797 |  | Mercedes S500 TC1797 |  | Mercedes SLS TC1797
AURIX
AUDO
confidential
NOT for hand-out

## Slide 82: AURIX™ Hybrid / EV solution key competence out of one hand
System Benefits
ISO 26262 ASIL-C/D compliant
Integrated resolver functionality for lower system cost
Enabling of sub-system integration (e.g. Hybrid Domain Control + Inverter Control + DC/DC)
Notes: Energy Efficiency for Combustion Engine Vehicles (from brochure)
Electronic automotive components are key to raising fuel efficiency levels and cutting emissions. The latest environment protection agency standards – Euro 5 and Euro 6 for passenger cars and Euro 3 and Euro 4 for motorcycles – are driving developments in advanced engine management. TriCore™-based products can be found in improved combustion technologies such as Homogeneous Charge Compression Ignition (HCCI) as well as in direct injection, smart turbocharger and valve actuation applications. They are also ideal for a range of innovative transmission technologies such as Double Clutch Transmission (DCT) and modern Continuous Variable Transmission (CVT).

## Slide 83: 48V Micro-Hybrid (Start/Stop and High-Efficiency Generator)
+48V from Battery
Supply IC
TLE4271-2G
TLE4291E
(including Watchdog)
3-Phase
Driver IC
TLE9180
H-Bridge
Driver IC
(TLE9180)
Rotor Position/Current Sense
Powertrain CAN
CAN
TLE7250GVIO
LIN
TLE7259-3GE
2Ch.
OptiMOS™-T2 100V
6x IPB180N10S4-02
Starter
Generator
Rotor Position
iGMR Sensor
TLE5012B
Current Sense
(Shunt Substitute)
2x TLE4990/98
OptiMOS™-T2 100V
4x IPD90N10S4-06
32-bit
Multicore/Lockstep
MCU
AURIX™
e.g. TC23xL
2MB / 200 MHz
24x
SAR
SENT
GTM
4x
QSPI
E-Ray
6x
CAN
ASCLIN
HSM
System Benefits
Full range of products ranging from voltage regulators, transceivers, sensors, microcontrollers and smart power drivers.
Leading-edge OptiMOS™ MOSFET technology combined with a robust package to deliver best in-class performance and outstanding current capacity
Higher alternator efficiency thanks to MOSFET rectification
Higher output current at low alternator RPM
Advanced modes supported: engine brake emulation, car sailing/coasting, electrical car launch

## Slide 84: 48V Micro-Hybrid (Start/Stop and High-Efficiency Generator)
+48V from Battery
Supply IC
TLE4271-2G
TLE4291E
(including Watchdog)
3-Phase
Driver IC
TLE9180
H-Bridge
Driver IC
(TLE9180)
Rotor Position/Current Sense
Powertrain CAN
CAN
TLE7250GVIO
LIN
TLE7259-3GE
2Ch.
OptiMOS™-T2 100V
6x IPB180N10S4-02
Starter
Generator
OptiMOS™-T2 100V
4x IPD90N10S4-06
32-bit
Multicore/Lockstep
MCU
AURIX™
e.g. TC23xL
2MB / 200 MHz
24x
SAR
SENT
GTM
4x
QSPI
E-Ray
6x
CAN
ASCLIN
HSM
Rotor Position
iGMR Sensor
TLE5012B
Current Sense
(Shunt Substitute)
2x TLE4990/98
System Benefits
Full range of products ranging from voltage regulators, transceivers, sensors, microcontrollers and smart power drivers.
Leading-edge OptiMOS™ MOSFET technology combined with a robust package to deliver best in-class performance and outstanding current capacity
Higher alternator efficiency thanks to MOSFET rectification
Higher output current at low alternator RPM
Advanced modes supported: engine brake emulation, car sailing/coasting, electrical car launch
Adapted!

## Slide 85: E-mobility: AURIXTM is an essential part of electrification, driving every e-application
Main Inverter
The inverter not only drives the electric motor, but is also used for regenerative braking and feeding energy back to the battery.
DC/DC Converter
The DC/DC converter charges the conventional 12 V power supply net from the high-voltage battery and replaces the former belt driven alternator.
Auxiliary Inverters/Converters
Instead of being belt-driven, auxiliaries like water pump, HVAC Compressor, PTC Heater, etc. also have to be driven by electric power. Inverters are needed to drive them smart and energy-efficient.
Battery Management
The battery management system controls battery state during charging and discharging. Intelligent functionality is needed to extend the battery lifetime, which has a considerable impact on the total cost of ownership. The State of Health (SoH), State of Charge (SoC) and Depth of Discharge (DoD) of the battery is permanently monitored.
On-board Charger
The battery block is charged via an AC/DC converter module. In the example shown here, an on-board unit charges the battery. Off-board and inductive charging solutions are also available.
HCU & Domain
In case of a hybrid car, Hybrid Control Unit or Vehicle Control Unit handle the inter-communication between sub-modules e.g. engine & hybrid motors inside a Hybrid EV. It can also serve as central gateway for Powertrain domain in the E/E architecture to ensure security communication between other domains.
AURIXTM for Main Inverter
Performs torque management & rotor positioning for efficient motor control
AURIXTM for DC/DC Converter
Handles the communication to AUTOSAR stack as well as execute control loops for multiple phases (up to 8)
AURIXTM for Auxiliary Inverters/Converters
Drives water pump, HVAC Compressor, PTC Heater as well as thermal management for more efficient energy use
AURIXTM for Battery Management
Monitors and reacts on State of Health(SoH), State of Charge(SoC) and Depth of Discharge (DoD) with the assistance of balancing ASICs; It prevents illegal manipulation both on system & battery packs via encrypted data-flow; It monitors system safety through SPI enabled ring topology.
AURIXTM for On-board Charger
Ensures galvanic insulation between mains and HV-battery,
As well as secure charge-billing, enables various power classes for flexible charging times
AURIXTM for HCU & Domain Control
handle the inter-communication between sub-modules e.g. engine & hybrid motors inside a Hybrid EV. Ensure secure communication & Software Over the Air(SOTA) as central gateway for Powertrain domain in the E/E architecture

## Slide 86
IGBT
Hybrid Pack
4x CAN
1x FlexRay
1x Ethernet
Lock step
200MHz
CPU0
200MHz
CPU2
Speed
&
Position
200MHz
CPU1
DS-ADC
SAR-
ADC
GTM
Lock step
PWM
PWM
PWM
1
DS-ADC
Integrated resolver to digital
1
2
Triple core
Best performance in the market
2
4
GTM timer
Dynamic motor control & tuning
4
1x I2C
5
5
CAN FD
Faster domain communication
Motor Control
Hybrid Domain Control
DC/DC converter
Resolver speed & position
Synchronised 3-phase
current measurement
PWM generation
Space vector modulation
Resolver interface
A
Resolver
PMSM
N
C
B
S
Resolver IC
Tamagawa
Or
AD2S1200
(H)EV Inverter System Solution
AURIX TC27x drives Integrated (H)EV Motor Control
AURIX TC2xx/3xx
32-bit
Microcontroller
6
6
Single voltage supply
Incl. safety features
8
8
next gen IGBT module:
20% smaller, 30% higher efficiency
Equal output power & faster assembly
EiceSIL ™
Driver IC
7
7
EICE SIL driver:
Integrated safety function
3
Safety up to ISO26262 ASIL D:
lock step, IOM…
3

## Slide 87: (H)EV – Main Inverter
Phase Current/
Voltage
Measurement
Power
Supply
Microcontroller
TC27x
LV Battery
Driver Stage
Power
Supply
Case Temperature
Measurement
NTC Measurement
DC-Link Capacitor
IGBT Stage
HV Battery
ϑ
System Benefits
Fully automotive-qualified product portfolio supporting a wide range of motors, generators and power classes
Highly-efficient 3-phase drive due to very low conducting losses even at high switching frequencies
Isolation-integrated in gate driver
Wide range of 32-bit microcontroller solutions dedicated to (H)EV applications with very cost effective resolver interface
Evaluation Kit available to reduce system development time

## Slide 88: (H)EV – Main Inverter
Phase Current/
Voltage
Measurement
Power
Supply
Microcontroller
TC27x
LV Battery
Driver Stage
Power
Supply
Case Temperature
Measurement
NTC Measurement
DC-Link Capacitor
IGBT Stage
HV Battery
ϑ
System Benefits
Fully automotive-qualified product portfolio supporting a wide range of motors, generators and power classes
Highly-efficient 3-phase drive due to very low conducting losses even at high switching frequencies
Isolation-integrated in gate driver
Wide range of 32-bit microcontroller solutions dedicated to (H)EV applications with very cost effective resolver interface
Evaluation Kit available to reduce system development time
Adapted!

## Slide 89
IFX offers whole system solution
From MCU, Sensor, Driver to Power module…
1
2
GTM
PWM generation
Motor control algorithm
3
32-bit Multi-core
Motor Control
Hybrid Domain Control
DC/DC converter
Resolver speed & position
ASC-LIN
High speed interface to position sensor
DS-ADC
Resolver positioning
4
1
2
3
4
5
Rotor position sensor
Reduce resolver BOM by $10
High accuracy in position angle
Easy to mount
Supporting ASIL
5

## Slide 90: HW resolver-to-digital interface today with AURIXTM TC2xx rotor positioning via sensor for TC3xx
Solution( Today):
  AURIX TC27x with highly accurate resolver-to-digital interface(DS-ADC)
  SW roto position algorithm with App note available
  concept on the road, NOW!
2 Options SOP>2020: resolver SW decoder or rotor position via sensor
Today
SOP >2020
Legacy
  Option 1(‘legacy’):
  Same as today but with AURIX TC38x
DHL eVan
Volvo V60
  Option 2(‘resolver-less’):
  End-of-shaft sensor for resolver replacement based on UART over CAN
  Save system cost by ca. $10-15
  Design in with EU OEMs
Option 2
SOP >2020
Resolver-less

## Slide 91: E-mobility: AURIXTM is an essential part of electrification, driving every e-application
Main Inverter
The inverter not only drives the electric motor, but is also used for regenerative braking and feeding energy back to the battery.
DC/DC Converter
The DC/DC converter charges the conventional 12 V power supply net from the high-voltage battery and replaces the former belt driven alternator.
Auxiliary Inverters/Converters
Instead of being belt-driven, auxiliaries like water pump, HVAC Compressor, PTC Heater, etc. also have to be driven by electric power. Inverters are needed to drive them smart and energy-efficient.
Battery Management
The battery management system controls battery state during charging and discharging. Intelligent functionality is needed to extend the battery lifetime, which has a considerable impact on the total cost of ownership. The State of Health (SoH), State of Charge (SoC) and Depth of Discharge (DoD) of the battery is permanently monitored.
On-board Charger
The battery block is charged via an AC/DC converter module. In the example shown here, an on-board unit charges the battery. Off-board and inductive charging solutions are also available.
HCU & Domain
In case of a hybrid car, Hybrid Control Unit or Vehicle Control Unit handle the inter-communication between sub-modules e.g. engine & hybrid motors inside a Hybrid EV. It can also serve as central gateway for Powertrain domain in the E/E architecture to ensure security communication between other domains.
AURIXTM for Main Inverter
Performs torque management & rotor positioning for efficient motor control
AURIXTM for DC/DC Converter
Handles the communication to AUTOSAR stack as well as execute control loops for multiple phases (up to 8)
AURIXTM for Auxiliary Inverters/Converters
Drives water pump, HVAC Compressor, PTC Heater as well as thermal management for more efficient energy use
AURIXTM for Battery Management
Monitors and reacts on State of Health(SoH), State of Charge(SoC) and Depth of Discharge (DoD) with the assistance of balancing ASICs; It prevents illegal manipulation both on system & battery packs via encrypted data-flow; It monitors system safety through SPI enabled ring topology.
AURIXTM for On-board Charger
Ensures galvanic insulation between mains and HV-battery,
As well as secure charge-billing, enables various power classes for flexible charging times
AURIXTM for HCU & Domain Control
handle the inter-communication between sub-modules e.g. engine & hybrid motors inside a Hybrid EV. Ensure secure communication & Software Over the Air(SOTA) as central gateway for Powertrain domain in the E/E architecture

## Slide 92: DC-DC converter General block diagram
Depending on the architecture, it is possible to find in the various solutions:
Several phases to add-up the required power.
  Up to 6-8 in 3KW for 48v applications
One uC (or DSP) or two uCs to control the systems
  1 uC for communication (AUTOSAR stack)
  1 uC dedicated for the control loop avoiding OS interruptions

## Slide 93: 48V/12V DC/DC Converter 8-phases version

## Slide 94: 1.5kW DC/DC Converter 4 phases demo-board
General Features
Bi-directional operation: BUCK & BOOST
No galvanic isolation
Power rating:
  Power board: 1.5kW
  AURIX board can control up to 2x 1.5kW board
Input: 36V…52V (24V…54V ext.)
Output: 8V…16V (ext. possible)
Efficiency >95%
Passive air cooling
Protection:
  overload
  reverse battery 12V
  short circuits internal and external
  voltage de-rating
Scalable 1.5kW
4-Phase DC/DC Board
AURIX
-based
8-phase
control
board
Notes: Topology: 8 phases, 100KHz PWM freq. for 48v (3KW)
First version running
Official documentation not yet available. Only documentation for internal use.
Update of the demonstrator planned for august 2017 which will include:
  Able to turn on-off phases
  Moving control to MCS

## Slide 95: E-mobility: AURIXTM is an essential part of electrification, driving every e-application
Main Inverter
The inverter not only drives the electric motor, but is also used for regenerative braking and feeding energy back to the battery.
DC/DC Converter
The DC/DC converter charges the conventional 12 V power supply net from the high-voltage battery and replaces the former belt driven alternator.
Auxiliary Inverters/Converters
Instead of being belt-driven, auxiliaries like water pump, HVAC Compressor, PTC Heater, etc. also have to be driven by electric power. Inverters are needed to drive them smart and energy-efficient.
Battery Management
The battery management system controls battery state during charging and discharging. Intelligent functionality is needed to extend the battery lifetime, which has a considerable impact on the total cost of ownership. The State of Health (SoH), State of Charge (SoC) and Depth of Discharge (DoD) of the battery is permanently monitored.
On-board Charger
The battery block is charged via an AC/DC converter module. In the example shown here, an on-board unit charges the battery. Off-board and inductive charging solutions are also available.
HCU & Domain
In case of a hybrid car, Hybrid Control Unit or Vehicle Control Unit handle the inter-communication between sub-modules e.g. engine & hybrid motors inside a Hybrid EV. It can also serve as central gateway for Powertrain domain in the E/E architecture to ensure security communication between other domains.
AURIXTM for Main Inverter
Performs torque management & rotor positioning for efficient motor control
AURIXTM for DC/DC Converter
Handles the communication to AUTOSAR stack as well as execute control loops for multiple phases (up to 8)
AURIXTM for Auxiliary Inverters/Converters
Drives water pump, HVAC Compressor, PTC Heater as well as thermal management for more efficient energy use
AURIXTM for Battery Management
Monitors and reacts on State of Health(SoH), State of Charge(SoC) and Depth of Discharge (DoD) with the assistance of balancing ASICs; It prevents illegal manipulation both on system & battery packs via encrypted data-flow; It monitors system safety through SPI enabled ring topology.
AURIXTM for On-board Charger
Ensures galvanic insulation between mains and HV-battery,
As well as secure charge-billing, enables various power classes for flexible charging times
AURIXTM for HCU & Domain Control
handle the inter-communication between sub-modules e.g. engine & hybrid motors inside a Hybrid EV. Ensure secure communication & Software Over the Air(SOTA) as central gateway for Powertrain domain in the E/E architecture

## Slide 96: P2S approach from Infineon
Infineon System provides additional features:
Ring mode topology
Extended transceiver supply
TC26x

## Slide 97: Smaller & Better! AURIXTM enables more efficient BMS solution
4x CAN
1x FlexRay
4x QSPI
Lock step
200MHz
CPU0
200MHz
CPU1
DS-ADC
SAR-
ADC
GTM
Checker core
PWM
PWM
PWM
1x I2C
e.g. TC26x
2.5MB Flash
240KB RAM
CSC ASIC
#5
CSC ASIC
#4
CSC ASIC
#3
CSC ASIC
#2
CSC ASIC
#1
Multi-Core &
Lockstep core
ASIL D compliant
1
1
2
Powerful GTM
Task triggering
2
-200 V
+200V
CSC ASIC
#6
SPI
SPI
SPI
SPI
SPI
SPI
IBCB
IBCB
IBCB
IBCB
IBCB
AURIX 65nm
Adapted!

## Slide 98
IGBT
Hybrid Pack
4x CAN
1x FlexRay
1x Ethernet
Lock step
200MHz
CPU0
200MHz
CPU2
Speed
&
Position
200MHz
CPU1
DS-ADC
SAR-
ADC
GTM
Lock step
PWM
PWM
PWM
1
DS-ADC
Integrated resolver to digital
1
2
Triple core
Best performance in the market
2
4
GTM timer
Dynamic motor control & tuning
4
1x I2C
5
5
CAN FD
Faster domain communication
Motor Control
Hybrid Domain Control
DC/DC converter
Resolver speed & position
Synchronised 3-phase
current measurement
PWM generation
Space vector modulation
Resolver interface
A
Resolver
PMSM
N
C
B
S
Resolver IC
Tamagawa
Or
AD2S1200
(H)EV Inverter System Solution
AURIXTM TC27x drives Integrated (H)EV Motor Control
AURIX TC2xx/3xx
32-bit
Microcontroller
6
6
Single voltage supply
Incl. safety features
8
8
next gen IGBT module:
20% smaller, 30% higher efficiency
Equal output power & faster assembly
EiceSIL ™
Driver IC
7
7
EICE SIL driver:
Integrated safety function
3
Safety up to ISO26262 ASIL D:
lock step, IOM…
3

## Slide 99: AURIX™ Family (H)EV Battery Management System
9x Series up to 8MB |  |  |  |  |  |  |  | 
7x Series up to 4MB |  |  |  |  |  |  |  | 
6x Series up to 2.5MB |  |  |  |  |  |  |  | 
3x Series up to 2 MB |  |  |  |  |  |  |  | 
2x Series up to 1 MB |  |  |  |  |  |  |  | 
1x Series up to 512 kB |  |  |  |  |  |  |  | 
 | TQFP-80 | TQFP-100 | LQFP-144 TQFP-144 | LQFP-176 | LFBGA-292 | BGA-416 | LFBGA-516 | Bare Die
All products include
standby power domain for long hour monitoring
CAN FD enabling fast communication
TC298T
300 MHz
TC267D
200 MHz
TC265D
200 MHz
TC275T
200 MHz
TC297T 300 MHz
TC234L
200 MHz
TC277T
200 MHz
TC224L/S
133 MHz
TC264D
200 MHz
TC223L/S
133 MHz
TC222L/S
133 MHz
TC213L/S
133 MHz
TC212L/S
133 MHz
Adapted!
TC233L
200 MHz
TC214L/S
133 MHz
TC237L
TC237LA/X
200 MHz
TC299T
300 MHz
BMS stack MCU
Monitoring battery stack SOH & SOC
HW security module (HSM) preventing battery pack manipulation & charge-billing verification
BMS main MCU
Overall dis/charging control
TC299T
300 MHz
TC299T
300 MHz

## Slide 100: E-mobility: AURIXTM is an essential part of electrification, driving every e-application
Main Inverter
The inverter not only drives the electric motor, but is also used for regenerative braking and feeding energy back to the battery.
DC/DC Converter
The DC/DC converter charges the conventional 12 V power supply net from the high-voltage battery and replaces the former belt driven alternator.
Auxiliary Inverters/Converters
Instead of being belt-driven, auxiliaries like water pump, HVAC Compressor, PTC Heater, etc. also have to be driven by electric power. Inverters are needed to drive them smart and energy-efficient.
Battery Management
The battery management system controls battery state during charging and discharging. Intelligent functionality is needed to extend the battery lifetime, which has a considerable impact on the total cost of ownership. The State of Health (SoH), State of Charge (SoC) and Depth of Discharge (DoD) of the battery is permanently monitored.
On-board Charger
The battery block is charged via an AC/DC converter module. In the example shown here, an on-board unit charges the battery. Off-board and inductive charging solutions are also available.
HCU & Domain
In case of a hybrid car, Hybrid Control Unit or Vehicle Control Unit handle the inter-communication between sub-modules e.g. engine & hybrid motors inside a Hybrid EV. It can also serve as central gateway for Powertrain domain in the E/E architecture to ensure security communication between other domains.
AURIXTM for Main Inverter
Performs torque management & rotor positioning for efficient motor control
AURIXTM for DC/DC Converter
Handles the communication to AUTOSAR stack as well as execute control loops for multiple phases (up to 8)
AURIXTM for Auxiliary Inverters/Converters
Drives water pump, HVAC Compressor, PTC Heater as well as thermal management for more efficient energy use
AURIXTM for Battery Management
Monitors and reacts on State of Health(SoH), State of Charge(SoC) and Depth of Discharge (DoD) with the assistance of balancing ASICs; It prevents illegal manipulation both on system & battery packs via encrypted data-flow; It monitors system safety through SPI enabled ring topology.
AURIXTM for On-board Charger
Ensures galvanic insulation between mains and HV-battery,
As well as secure charge-billing, enables various power classes for flexible charging times
AURIXTM for HCU & Domain Control
handle the inter-communication between sub-modules e.g. engine & hybrid motors inside a Hybrid EV. Ensure secure communication & Software Over the Air(SOTA) as central gateway for Powertrain domain in the E/E architecture

## Slide 101: AURIX™ - Software Mapping for OBC Success story of SW mapping in 2 cores
TC 1.6P
CPU0
FPU
64KB PSPR
32KB PCACHE
192KB DSPR
16KB DCACHE
Checker Core
DFlash
PFlash
LMU
DMA
SFI
Bridge
HSSL
HSCT
MSC
FCE
HSM
Port
IOM
SCU
System Resource Interconnect
CPU1
DAM
Package Variants
T/LQFP 144
LQFP 176
LFBGA 292
preliminary - subject to change
High temperature devices available on request
2 Cores with 196kB DSPR
ETH MAC
Prim ADC
FCOMP
Sec ADC
EDS ADC
GTM
STM
GPT
CCU6
ERAY
MCM CAN
QSPI
ASC LIN
SENT
I2C
PSI5
PSI5S
System Peripheral Bus
EVADC
Three “separated SW Domains”
Autosar with communication and initialization
  Ensure compatibility and conformance to standards
Non-Autosar with DC/DC & PFC control
  Ensure fast real-time control
Security Domain in HSM
  Key handling
  Encryption/decryption
Advantages:
Highest possible integration
One MCU covering whole application
Statically separated by hardware measures
  Eases SW development
  Eases safety concept
  Eases Security concept
Notes: Update:
Bare Die Tj max 170
BMU REMOVED
Flash Architecture

## Slide 102: Infrastructure General Diagram
3kW
3kW
3kW
0 - 4MW
per module
350kW
fast charging
on board charging
control, payment
&
balancing unit
0 - 13MW
local protected network (wired or wireless)
global protected network
$
$
$
inner ring

## Slide 103: Fast charging solutions
PFC
Power Factor Correction
DC DC
Isolated
400Vac
690Vdc
200Vdc
-900Vdc
-900Vdc
1
PFC
Power Factor Correction
DC DC
Non Isolated
400Vac
690Vdc
200Vdc
-900Vdc
-900Vdc
PFC
Power Factor Correction
DC DC
Non Isolated
400Vac
690Vdc
200Vdc
-900Vdc
-900Vdc
Isolated Transformer
10kVac
20kVac
2

## Slide 104: Fast charging solutions- three phase
PFC
Power Factor Correction
DC DC
Isolated
400Vac
690Vdc
200Vdc
-900Vdc
-900Vdc
1
Vienna Rectifier
Voltage Source Inverter
Unidirectional
Silicon Carbide MOS
Insulated Gate Bipolar Transistor
Super Junction MOS

## Slide 105: On board charging solutions
PFC
Power Factor Correction
DC DC
Isolated
230Vac
390Vdc
200Vdc
-420Vdc
-900Vdc
1
PFC
Power Factor Correction
DC DC
Isolated
400Vac
690Vdc
200Vdc
-900Vdc
-900Vdc
2
The On board charger must be bidirectional
The protected communication must be enabled

## Slide 106: On board charging solutions – single phase
PFC
Power Factor Correction
DC DC
Isolated
230Vac
390Vdc
200Vdc
-420Vdc
-900Vdc
1
Triangular Current Mode (TCM)
Totem Pole PFC
Super Junction MOS
Silicon Carbide MOS
Gallium Nitride HEMT
Insulated Gate Bipolar Transistor
Bidirectional

## Slide 107: On board charging solutions – three phase
T-Type Inverter
Voltage Source Inverter
Silicon Carbide MOS
Insulated Gate Bipolar Transistor
Silicon Carbide MOS
Insulated Gate Bipolar Transistor
PFC
Power Factor Correction
DC DC
Isolated
400Vac
690Vdc
200Vdc
-900Vdc
-900Vdc
2
Bidirectional

## Slide 108: AURIX™ Family (H)EV Control
9x Series up to 8 MB |  |  |  |  |  |  |  | 
7x Series up to 4 MB |  |  |  |  |  |  |  | 
6x Series up to 2.5 MB |  |  |  |  |  |  |  | 
3x Series up to 2 MB |  |  |  |  |  |  |  | 
2x Series up to 1 MB |  |  |  |  |  |  |  | 
1x Series up to 512 KB |  |  |  |  |  |  |  | 
 | TQFP-80 | TQFP-100 | LQFP-144 TQFP-144 | LQFP-176 | LFBGA-292 | BGA-416 | LFBGA-516 | Bare Die
TC270T
200 MHz
TC260D
200 MHz
TC212L/S
133 MHz
TC223L/S
133 MHz
TC233L
200 MHz
TC234L
200 MHz
TC224L/S
133 MHz
TC213L/S
133 MHz
TC277T
200 MHz
TC275T
200 MHz
Hybrid Control
Torque management and communication
Tailored Multi Drive PWM generation
TC265D
200 MHz
TC264D
200 MHz
Basic E-Motor Drive
3-phase PMSM or BLDC Motor drive
TC299T
300 MHz
Integrated Hybrid Control
Torque management & Net Communication
3-phase e-drive control for PMSM FOC & Resolver Interface
MultiCore Architecture with superior multi motor control performance
TC298T
300 MHz
TC297T
300 MHz
Note: Divers OEM (H)EV inverter topologies may integrate:
DC/DC Control Functions
Charge Control Functions
48V E-Motor control
Motor control for. 48V, micro Hybrid
TC267D
200 MHz
TC237L
200 MHz
TC222L/S
133 MHz
TC214L/S
133 MHz
Notes: Update 11/13: 4x series devices

## Slide 109: AURIX™ Family (H)EV DC-DC
9x Series up to 8 MB |  |  |  |  |  |  |  | 
7x Series up to 4 MB |  |  |  |  |  |  |  | 
6x Series up to 2.5 MB |  |  |  |  |  |  |  | 
3x Series up to 2 MB |  |  |  |  |  |  |  | 
2x Series up to 1 MB |  |  |  |  |  |  |  | 
1x Series up to 512 KB |  |  |  |  |  |  |  | 
 | TQFP-80 | TQFP-100 | LQFP-144 TQFP-144 | LQFP-176 | LFBGA-292 | BGA-416 | LFBGA-516 | Bare Die
TC270T
200 MHz
TC260D
200 MHz
TC212L/S
133 MHz
TC223L/S
133 MHz
TC233L
200 MHz
TC234L
200 MHz
TC224L/S
133 MHz
TC213L/S
133 MHz
TC265D
200 MHz
TC264D
200 MHz
TC299T
300 MHz
TC298T
300 MHz
TC297T
300 MHz
TC267D
200 MHz
TC237L
200 MHz
TC222L/S
133 MHz
TC214L/S
133 MHz
DCDC Control
HV-12V
HV-LV e.g. Motor/BMS
48V-12V
Board net stabilization
TC277T
200 MHz
TC275T
200 MHz
DCDC Control
(H)EV Integrated DCDC control
Notes: Update 11/13: 4x series devices

## Slide 110: Table of contents
Infineon Microcontroller
1
  3
AURIX TC2xx PDH Support model
2
  14
AURIX TC2xx Overview
3
  17
AURIX TC2xx Feature Details
4
  31
AURIX TC2xx Functional Safety
5
  51
AURIX TC2xx Security
6
  64
AURIX TC2xx Powertrain
7
  75
AURIX TC2xx xEV
8
  79
AURIX TC2xx CAV
9
110
AURIX TC2xx Benchmarking vs. Competition
10
  118
AURIX TC2xx SW & Tools
11
  127

## Slide 111: Megatrends to increase profitability of commercial vehicles and truck fleets
Powerful Energy Storage
Powertrain Redundancy
Megatrends for Commercial Vehicles
Functional Safety
IT-Security
Increasing E/E complexity
Energy distribution
Diagnosis
Fail operational
48 V for recuperation
Predictive Powertrain Control
Enhanced Energy Recuperation
Electrification of side loads
Electrification of Powertrain
Challenges for truck OEMS
FUEL EFFICENCY
Enhanced Emergency Braking
Enhanced Highway Pilot
V2V – Platooning
Remote Control Maneuver
SAFETY & ADAS
Networked Information, Navigation Info's
Vehicle to Infrastructure Connectivity
CONNEC- TIVITY
Sensor Fusion
System Redundancy
Increased Data Output &
secure Data- and energy supply
EHPS

## Slide 112: AURIXTM adresses CAV Requirements and Challenges
  External Memory Extension
  Lots of IOs
  Safety
Expensive external RAMs
Short life cycles
Design complexity
No memory integrity support
Hundreds of valves, actuators and LEDs
Many analog signals to be measured
Communication interfaces
Increasingly rigurous safety standards
Expensive dual channel approach
Tedious work until certification
  Special devices with extended SRAM
  Up to 2.7 MB SRAM
  Different packages up to 516 pins
  Multiple ADCs, communication interfaces
  Family safety concept, IEC61508
  Lockstep
  Safety support
Notes: What do you mean with short life cycles?

## Slide 113: Leading OEM AURIXTM Fitments up to 10 AURIXTM driving Powertrain & E-mobility
Diesel Injection
4/6cyl.
4cyl Gasoline Injection
DCT
9 speed
On Board Charger
3.6kw & 11kw
48V & HV Battery Management System
confidential
NOT for hand-out
Traditional Powertrain
E-Mobility
TC38x
TC27x
TC23x
TC29x
TC21x
HV
Inverter & DCDC
48V Integrated/Belt Starter Generator
Central Powertrain Controller
Domain
TC26x

## Slide 114: #1 Microcontroller Supplier in Powertrain Engine for Light Vehicles & Trucks
Chart: 
| IFX | Others
Sales | 46 | 54
2016 TriCoreTM
Market Share
EMS Truck*
Chart: 
| IFX | Others
Sales | 39 | 61
2016 TriCoreTM
Market Share
EMS Light Vehicle*
Source: IFX assessment combined with market figures, latter based on IHS (11.2016) , Truck >6t, light vehicle incl. pick-up trucks <6t
confidential
NOT for hand-out
TC29x
TC29x
TC29x
TC179x
TC27x/6x
TC29x
TC179x
TC176x
TC176x
TC176x
AURIX
AUDO

## Slide 115: AURIX™ versatile architecture for various CAV applications
AURIXTM – Safety joins Performance
AURIX™ for CAV Success Stories
IEC 61508
24V Braking Platform Key Selling Points:
Lockstep & safety requirements
24V Gateway / BCM Platform
Key Selling Points:
Performance, SRAM & CAN FD
Engine & Transmission Control Units
Key Selling Points:
Tailored Powertrain features ,Scalability in packages, ext. SRAM
Central Vehicle Manager Key Selling Points:
Performance, I/O scalability, Safety
Notes: Truck OEM develop software inhoues. Tier1 deliver only hardware
Engine control unit :
GTM Timers for up to 16 cylinder control
DSADC for knock detection, in cylinder pressure measurement
No painful optimization of code needed
Knorr Bremse :
24V Braking Platform Required MCU features:
Lockstep & safety requirements
Devices :
TC265x, TC21x/TC22x/TC23x
24V Gateyway Platform
Required MCU features:
high performance, RAM & CAN FD
Device:
TC275
VOLVO Trucks:
Engine & Transmission Control Units
Reuqired MCU features:
Tailored Powertrain features ,scalability in packages, 2.7 Mb SRAM
Devices:
TC29x for high end markets
TC27x for cost effective markets
MAN:
Central Vehicle Manager/ Required MCU features:
Performance, I/O scalability, Device:
TC297, TC277

## Slide 116: AURIX™ versatile architecture for various CAV applications
AURIXTM – Safety joins Performance
AURIX™ for CAV Success Stories
IEC 61508
NG Forklift ECU Platform
Key Selling Points:
Performance, Safety & CAN FD
CAN Ethernet Gateway
Key Selling Points:
Performance, CAN FD, scalability
Various other applications Key Selling Points:
Performance, Scalability, Safety , ext. SRAM
Notes: Truck OEM develop software inhoues. Tier1 deliver only hardware
Engine control unit :
GTM Timers for up to 16 cylinder control
DSADC for knock detection, in cylinder pressure measurement
No painful optimization of code needed
Knorr Bremse :
24V Braking Platform Required MCU features:
Lockstep & safety requirements
Devices :
TC265x, TC21x/TC22x/TC23x
24V Gateyway Platform
Required MCU features:
high performance, RAM & CAN FD
Device:
TC275
VOLVO Trucks:
Engine & Transmission Control Units
Reuqired MCU features:
Tailored Powertrain features ,scalability in packages, 2.7 Mb SRAM
Devices:
TC29x for high end markets
TC27x for cost effective markets
MAN:
Central Vehicle Manager/ Required MCU features:
Performance, I/O scalability, Device:
TC297, TC277

## Slide 117: AURIX™ for Trucks – Customer and value proposition Summary
Infineon provides system know how and optimized components for system offering (AURIXTM, supply, sensors, 3-phase driver, transceiver)
Performance is key parameter: AURIXTM microcontrollers provide highest application performance in the market in combination with ISO26262 ASIL-D safety capabilities throughout the family.
Scalability – AURIXTM microcontrollers provide highest level of scalability for customers with max. software re-use possibility through out the family :
TC 1.6 binary compatibility
Unified set of peripherals across the device family
Pin compatibility between different devices
Unified safety concept
AURIXTM microcontrollers are compatible with latest OEM requirements :
  CAN-FD (optional)
  Hardware Security Module (optional)

## Slide 118: Table of contents
Infineon Microcontroller
1
  3
AURIX TC2xx PDH Support model
2
  14
AURIX TC2xx Overview
3
  17
AURIX TC2xx Feature Details
4
  31
AURIX TC2xx Functional Safety
5
  51
AURIX TC2xx Security
6
  64
AURIX TC2xx Powertrain
7
  75
AURIX TC2xx xEV
8
  79
AURIX TC2xx CAV
9
  110
AURIX TC2xx Benchmarking vs. Competition
10
118
AURIX TC2xx SW & Tools
11
  127

## Slide 119: Exceptional Performance
Monaco
e200z335 @80Mhz
Andorra
e200z4
@150MHz
Mamba
e200z7 @266Mhz
SH7286
SH2A @100Mhz
Estimation
SH2A @200Mhz
TC1767/24
TC1.3.1
@80Mhz
TC1797/82
TC1.3.1
@180Mhz
TC179x
TC1.6
@300Mhz
152%
152%
100%
46%
81%
45%
113%
80%
28%
Competitor A
Competitor B
Infineon
TC179x
TC1.6
@200Mhz
113%
TC1767/28
TC1.3.1
@133Mhz
74%
Performance benchmark based on the application code for a
4 cylinder direct injection engine management system
Estimation
1.5x
TC1.6P
@300Mhz
228%
TC29xT
Estimation
1.5x
TC1.6P
@200Mhz
170%
TC27xT
w/o peripheral core (TC1.6E)
Dual core utilization factor = 1.5

## Slide 120: TriCore – best in class FOC execution time, real user case, non-optimized code
Chart: 
 | 13 | 21 | 32 | 40 | 75 | 105
Benchmarking source: based on leading tier 1, Dual mototcontrol in use
Competitor B
@120Mhz
TC1782
@180Mhz
Competitor A
@120Mhz
Competitor C
@100Mhz
AURIX TC23x
@200Mhz
µs
AURIX TC27x
@200Mhz
Faster execution time = better performance
8
25

## Slide 121: AURIX™ - Ahead of competition multiple reasons for AURIXTM as performance lead
 | Competitor A | Competitor B | IFX 65nm AURIX TC29xx | Benefits
Max Flash / RAM / CPU-cores | 8MB/1MB/3cores | 4MB / 1MB /2cores | 8MB/2,7MB/3cores | 
Superscalar core | Yes (partial) | Yes (full) | Yes (partial) | 
Pipeline length | 7 | 8 | 6 | ++ performance shorter pipeline
High performance tightly coupled RAM | Yes (64bit bus) | No (32bit bus) | Yes (64bit bus) | ++ performance for context switch, function call/return
Multi core architecture with data caches | Yes | No | Yes | + performance when dealing with flash based variables
RAM scheme for multicore | Small local RAMs (0 wait state core RAM) | Small local RAMs (0 wait state core RAM) | Big local RAMs | ++ performance in real system (low bandwidth with central RAM)
Max CPU clock | 300MHz | 320MHz | 300MHz | 
Program RAM for intensive loops and fast reaction vs interrupts | No | No | Yes | ++ performance in real systems
Flash bandwidth for multicore versions | 1280MB/sec total | ?? | 1280MB/sec Per core | ++ performance in real system

## Slide 122: AURIXTM competitive advantages for motor control ahead of competition e.g. RENESAS
Real EPS customer benchmark for evaluation of execution time and code size
Benchmark done for
  AURIX TC23x at 132MHz
  Reference used was CPU „Competitor“ at 160MHz
Results:
3.5% faster
10% faster
TC23x execution up to 10% faster at 132MHz vs. competition device at 160MHz
TC23x code size up to 18% smaller at comparable execution time
18,6% smaller
Less power consumption, less power dissipation, less cost
More head room for performance needs

## Slide 123: Infineon AURIXTM TC23x competitive advantages ahead of competition
 | TC23x | TC23x Extended | Competitor | Competitive Advantage
CPU |  |  |  | 
Clock Frequency | 200 MHz | 200 MHz | 160 MHz | 
Memories |  |  |  | 
Flash Size | 2M | 2M | 1M | 
0 Wait-state SRAM in kB | 192 | 192 | 0 | ++ Performance
Total RAM in kB | 224 | 512 | 128 | + Performance
Supply concept |  |  |  | 
Integrated switch cap DCDC (no coil for low cost BOM) | Yes | Yes | No | ++ Cost ++ Consumption
Analog Frontend |  |  |  | 
5V ADC | Yes | Yes | No | + Accuracy + Cost
Communication & Security |  |  |  | 
CAN (CANFD) | 6 (4 FD) | 6 (4 FD) | 3 (no FD) | ++ Performance + Compliancy
Hardware Security Module | Yes | Yes | No | ++ Security
Package and Temperature |  |  |  | 
Ambient Temperature | -40 to 150 | -40 to 150 | -40 to 125 | ++ Quality
Package | TQFP100 TQFP144 BGA292 | TQFP144 | LQFP144 BGA292 | ++ Fail Operational ++ Cost

## Slide 124: Infineon Safety Computing platform advantages
 | Competitor Product | TC23x
Freedom from interference |  | 
Memory Protection Unit to isolate the safing task |  | 
CRC unit to protect the data of the safing task |  | 
Common cause of failure |  | 
Challenge / response based watchdog |  | 
HW for stack over / under flow |  | 
High coverage CPU core self tests supported by HW channel |  | 
Power-on self tests, Run time self tests |  | 
Independent channel for test result monitoring |  | 
90% minimum coverage proven according to ISO26262 method |  | 
ECC or parity protection on each memory |  | 
HW diversity (no diverse SW is required for) |  | 
Field proven fault management SW |  | 
Single supply MCU (additional DCDC required for 140 degree ambient) |  | 
0 wait state RAM |  | 
5v 12bits ADC (3,3v requires high quality PCB) | 3,3v only | 
Current consumption at 80MHz (no GPIO) | 510mA DCDC required even at 120C° | 50mA

## Slide 125: DMIPS AURIXTM
210
TC1.6E @80MHz
136
460
1380
medium optimization
aggressive optimization
aggressive and whole program optimization
340
TC1.6E @200MHz
TC1.6P @200MHz
TC1.6P @300MHz
Notes: The Dhrystone 2.1 (DMIPS/MHz) is a tiny code, which fits to Code Cache and Data Cache. The Profiling information of the shows a heavy load on string library functions. Cross Module optimization can inline the libraries and other function calls.
The aggressive optimizations are not applicable to real case compiler usage
TC1.6E DMIPS/MHz = 1.4-1.7 - TC1.6P DMIPS/MHz = 1.5-2.3
TC27x: 1x1.6E+2x1.6P @200MHz
TC29x: 3x1.6P @ 300MHz
690
2xTC1.6P @300MHz
3xTC1.6P @300MHz
2070

## Slide 126: EEMBC Automarks AURIXTM
Notes: The improved Automark figures for automotive EEMBC benchmark results are based on synthetic optimized settings
    these figures therefore are not applicable for real automotive application
The aggressive optimizations are not applicable to real case compiler usage
210
TC1.6E @80MHz
71
209
325
medium optimization
aggressive optimization
aggressive and whole program optimization
115
TC1.6E @130MHz
TC1.6P @200MHz
TC1.6P @300MHz

## Slide 127: Table of contents
Infineon Microcontroller
1
  3
AURIX TC2xx PDH Support model
2
  14
AURIX TC2xx Overview
3
  17
AURIX TC2xx Feature Details
4
  31
AURIX TC2xx Functional Safety
5
  51
AURIX TC2xx Security
6
  64
AURIX TC2xx Powertrain
7
  75
AURIX TC2xx xEV
8
  79
AURIX TC2xx CAV
9
  110
AURIX TC2xx Benchmarking vs. Competition
10
  118
AURIX TC2xx SW & Tools
11
127

## Slide 128: AURIXTM Tool Ecosystem The right partner and tool at each development stage
Embedded Software
Virtual/Rapid Prototyping
Compilers
Operating System
Multicore Analysis
Flash Programing & Tools
Calibration
Emulators/Debugging/Test
Auto-code generator
V
SW development
&
integration
Validation
Prototyping
Verification
&
Calibration
Modeling
&
Simulation
Trainings & Services
SW verification & Testing

## Slide 129: Infineon AURIXTM Software offering Reduction of customer SW development
Commercial Value Software
SHE+ security driver:
  Supporting latest security requirements
Commercial Basic Software
AUTOSAR MCAL:
  MC-ISAR Basic (Base, MEM, COM Basic)
  MC-ISAR COM Enhanced
  MCAL Complex Driver MCD and Demo code
Safety driver: to support HW safety features and external watch dogs
Auxiliary Tools and Software
C Model
Simulink model (RADAR only)
Software Design Services
Customer specific driver
On customer request
AURIX™
Software
Free tool/ example code
iLLD: Infineon low level driver
ACT : AURIX configuration tool
FreeOSEK
Free compiler
Free debugger

## Slide 130: Infineon Software Product Overview
Hardware
Microcontroller Abstraction Drivers
Application SW
Appl. SW
Operation SW
HW
Software
Safety Driver
Security Driver
Libraries
Applications Driver
Focus areas
Via 3rd parties
System Software
(Services, OS, Communication, Memory Manager etc.)
Microcontroller Abstraction Drivers
  AUTOSAR MCAL according ASRv3/4
  AUTOSAR libraries
Safety Driver
  PRO-SILTM SafeTlib to enable ISO 26262 application
Security Driver
  HSM driver
System Software
  AUTOSAR suites from 3rd parties

## Slide 131: Infineon AUTOSAR MCAL Driver MC-ISAR Product Overview
AUTOSAR in production since 2009
Microcontroller
Infineon MC-ISAR driver (MicroController Infineon Software ARchitecture)
Enabled via partners
MCU
WDG
RAM
Test
PORT
ADC
DIO
MCAL
CAN
GPT
PWM
ICU
On-Board Device Abstraction
Memory Services
I/O Hardware Abstraction
Memory Abstrac- tion
Communication Abstraction
Communication Services
Application Layer
SPI
CanTrcv
FEE
LIN
System Services
AUTOSAR Run Time Environment (RTE)
System Services
Complex Device Driver
SCI
MEM Check
…
FADC
Flex Ray
MC-ISAR MicroController – Infineon Software ARchitecture
MC-ISAR: MCU, WDG, GPT, SPI, PORT, DIO, ICU, PWM, ADC
MC-ISAR COM Basic: CAN, CanTrcv, LIN
MC-ISAR COM Enhanced: FlexRay, Ethernet
MC-ISAR MEM: FLASH, FEE
MC-ISAR MCAL CD: SCI, MEMCheck, FADC, etc. for TriCore™
FLS
Supported AUTOSAR releases and devices:
    V3.2, V4.03 available
    ISO26262 support
    Support of AS.V4.1
    AS. 4.2.1 on request
ISO26262 support up to ASIL-B
CMM L3 process
Complex driver package for SHE+, Safety Lib, etc.
Delivery packages includes: source code, user manual, Tresos configuration tool
Notes: CMM L3 Prozess? Software Entwicklungs Quali Standard
Non Standardized Module -
Autosar (BasicSoftWare) Suite?
Wir bieten die blau vorgehobenen MCAL Treiber an
Aufgeteilt in die einzelnen Module
Für unsere Micros unterstützen wir Autosar V3.2 und V4.0 an
Zusätzlich complex driver für nicht standardisierte Module
Autosar Basic Software ist zu beziehen über unsere Partner -> hier auch noch ETAS einfügen

## Slide 132: Free TriCore™ Entry Tool Chain Provider Hightec
This free of charge tooling package provides all required features to develop and test software for TriCoreTM and AURIXTM . The tool can be used with all available TriCoreTM and AURIXTM StarterKits and Application Boards
  Eclipse based IDE
  Project wizard to easy define the project properties for device and board support
  High performant GNU C compiler
  Integrated source level debugger
  On-chip Flash programming support
  http://free-entry-toolchain.hightec-rt.com
Free of charge

## Slide 133: Free TASKING Pin Mapper for AURIXTM Provider Tasking
The Free TASKING Pin Mapper for AURIX enables both novice and expert users to quickly configure AURIX microcontrollers by making connections between port pins and peripherals.
Key features:
Eclipse based GUI with built-in knowledge about AURIX devices and packages.
The Pin Mapper creates:
  device initialization code in ISO-C format
  a spreadsheet (CVS) file for project documentation
  a schematic symbol block that can be imported by PCB design tools
Supported TriCore Devices:
  AURIX Family (TC22x, TC23x, TC26x,
  TC27x, TC29x)
  AURIX 2G Family (TC38x, TC39x).
Request the Free TASKING Pin Mapper
for AURIX through this form.
Free of charge

## Slide 134: Free AURIXTM Configuration Free Flash Loader: Infineon MemTool
Infineon provides free Flash Loader SW that supports various connection interfaces
Data communication via UART, DAS (DAP,JTAG)
Flash support for AURIX™,
Batch-Mode functionality
Automatic COM port detection
On-chip Flash protection features supported
Free of charge
www.infineon.com/memtool

## Slide 135: Multicore Support Best-in-class On Automotive Applications
Cutting edge technology on multicore powered by AURIX
Specialized Multicore architecture
Tailored customer support
Multi-core know-how
    Real-Time capable hardware
    Support of both Asymmetric and Symmetric Multi-Processing
    HW and SW support for virtualization
    ISO26262 ASIL-D compliant
    Large experience in safety app. and multicore architectures
    Specialized team for multicore on each AURIX target app.
    Strong partnership with highly specialized multicore tool partners
Best support at every development stage
    Support through tool partners on multicore SW development
    Support on critical parts of SW development related to AURIX architecture
    Dedicated application notes covering topics like
      Methods for synchronization and data exchange
      Spinlocks and others related to performance impact on multi-core
    Powerful multicore tools to get the best performance out of AURIX
Specialized Multicore workforce

## Slide 136: Using AURIXTM multicore efficiently Basic Workflow
Analyze the end application
Decide optimization objectives and constraints
Gain basic multicore know-how
Understand AURIX multicore architecture
Acquire multicore knowledge
Analyze the use-case
Multicore SW Design
Develop the multicore SW
Evaluate the performance
Optimize the distribution
Assign cores
Creation of memory mapping
Design methods of communication and synchronization among cores
Implement the multicore SW designed and multicore mechanisms
Debug
Trace
Measure timing and access
In case the achieved performance is not sufficient, repeat from step 3
Universities / academic literature
1
2
3
4
5
6

## Slide 137: Using AURIX multicore efficiently Basic Workflow
Acquire multicore knowledge
Analyze the use-case
Multicore SW Design
Develop the multicore SW
Evaluate the performance
Optimize the distribution
1
2
3
4
5
6
METHODOLOGY
Static Analysis
Runnables dependency analysis
Dynamic Analysis
Scheduling analysis
CPU load analysis
TARGET
Create scenarios of memory mapping, core assignment and method of communication that fulfills the requirements and constrains set.
Analyze the end application
Decide optimization objectives and constraints
Assign cores
Creation of memory mapping
Design methods of communication and synchronization among cores
TASKS
2
3

## Slide 138: Using AURIXTM multicore efficiently Basic Workflow
Acquire multicore knowledge
Analyze the use-case
Multicore SW Design
Develop the multicore SW
Evaluate the performance
Optimize the distribution
1
2
3
4
5
6
TARGET
Compare the performance of all the SW architecture approaches (scenarios) that have been created
METHODOLOGY
Comparison of the implemented SW architectures through optimization tools
TASKS
Analyze results based on the timing and scheduling implementations
In case the achieved performance is not satisfactory, create another scenario (SW architecture) based on the results obtained.

## Slide 139: AURIXTM Virtual Models
Availability of virtual model
The AURIXTM VM simulate the entire µC, i.e. TriCore and most peripherals. The models are cycle approximate and the binary code developed in the VM can be executed without changes on the silicon and vice versa.
Software Advantages
  Enables early SW development (before EES is available)
  Enables easier SW outsourcing as no HW has to be exchanged
  High flexibility in SW verification
    Easy error/fault injection
    Easier insight into device behavior, for example GTM waveforms.
System Benefits
  SW quality improvement
  Reduce risk of delay, by early start of development
  Improves time to market
Virtual model (VM)
SW development timeline
Synopsys Virtualizer
ASTC VLAB
OR
Availability of the actual device
~ 6 months*
Availability of AUTOSAR along with the virtual model is under consideration
* Target availability. Subject to the required peripheral set

## Slide 140: AURIX™ kits and application boards available for ordering

## Slide 141: 15W Automotive in-cabin Wireless Charger Reference design
„The Beast“, the 15W Automotive in-cabin Wireless Charger reference design featuring AURIX™ TC212SC is available and can be ordered via ISAR: KIT_AURIX_TC21_SC
It is Qi qualified and listed on the WPC: https://www.wirelesspowerconsortium.com/products/4699
The technical documentation, including complete BOM and schematics is available on MyICP (under NDA) -> MyICP registration guide: https://www.infineon.com/MyICPreg
Find more information on our website: https://www.infineon.com/cms/en/product/evaluation-boards/kit_aurix_tc21_sc/

## Slide 142: BLDC development kit HW, SW, Documentation - supports reduced time to market

## Slide 143: 24GHz RADAR development platform Enabling BSD application
All documents to produce hardware (Gerber-files, BOM, schematics)
Source code for AURIX and PC-Software (GUI)
Documentation including protocol description and start-up guide
BGT24ATR12
TC264D
AURIX
Prozessor
Ethernet
(RJ-45)
Power
/CAN
1 TX-antenna (10x60° angle)
2 RX-antennas (10x85° angle)
Tracking of objects up to 50m.

## Slide 144: 24 GHz radar for Short Range Radar Optimized Infineon system solution
ECU features
Sequential lobbing by switching received signals
Networking bus
  Private CAN
  Opt. FlexRay
Small PCB footprint
Key advantages
High integration leads to significant cost savings
High integration leads to reduced complexity
ISO 26262 compliance supports safe input for functions such as emergency braking
Innovative supply concept
SPI
4x
ADCs
Acquisition
RAM
TriCore™
TC26x
+12V from Battery
24 GHZ
Short Range Radar
TLF35584 Safety Power Supply
with integ. WD
Low noise supply
BGT24AR2
CAN
Transceiver
TLE 6251
TLE7250
FlexRay
Transceiver
TLE 9221
FlexRay-Bus
200MHz
input timer
FFT engine
LPF +
LNA + Muxes
BGT24ATR12
Coarse
Fibne
optional PLL
3,3v
5v CAN
5v ADC-ref
5v LNAs
3,3v / 600mA

## Slide 145: TLF35584QVVS1/VS2 plus AURIX™ TriBoard Evaluation Environment
TLF35584-Evaluation-Boards (Green)
  Equipped either with 3V3- or 5V-variant
  Can be adapted to high- and low-switching frequency
AURIX™TriBoard (Red)
  For TLF35584-configuration
  Stack-concept
  GUI
    Parameter setting
    Monitoring functions
    SPI-communication logging
    Register modification
    Flag control