## Slide 1: AIROC™ CYW54590/54591 Dual-Band Wi-Fi 5 + Bluetooth® Combo SoC Reliable solution for IoT applications needing Wi-Fi 5
Product brief
CYW5459x is a complete dual-band (2.4 GHz and 5 GHz) Wi-Fi 5 2×2 MIMO MAC/PHY/Radio System-on-Chip. This Wi-Fi 5 single chip device provides a high level of integration with a dual-stream IEEE 802.11ac MAC/baseband/radio and Bluetooth® 5.3. In IEEE 802.11ac mode, the WLAN operation supports rates of MCS0–MCS9 (up to 256 QAM) in 20 MHz, 40 MHz, and 80 MHz channels for data rates up to 867 Mbps. In addition, all the rates in IEEE 802.11a/b/g/n are supported. Included on-chip Wi-Fi 5 are the 2.4 GHz and 5 GHz transmit power amplifiers and receive low-noise amplifiers. The WLAN operation on the CYW54590 supports 2x2 MIMO operations as well as two fully simultaneous SISO channels; one in 2.4 GHz and the other in 5 GHz enabling dual-band real simultaneous dual-band (RSDB) operation.
For the Wi-Fi operation, the device interfaces to a host SoC processor through a PCIe v3.0-compliant interface running at Gen1 speed, and an SDIO v3.0 interface that can operate in 4b or 1b modes. For the Bluetooth® operation, host interface is through a high-speed 4- wire UART interface and PCM interface for audio.
In addition, the CYW5459x implements highly sophisticated enhanced collaborative coexistence hardware mechanisms and algorithms that ensure that Wi-Fi and Bluetooth® collaboration is optimized for maximum performance. Coexistence support for external radios (such as LTE cellular and GPS) is provided via an external interface. As a result, enhanced overall quality for simultaneous voice, video, and data transmission on a commercial/consumer systems is achieved.
CYW5459x enables fast data streams with minimal latency, making it ideal for high definition video streaming and audio streaming applications, such as smart speakers, gaming, VR, and smart TVs. The throughput of the device also makes it ideal for applications demanding higher throughput like WLAN, industrial gateways and edge computing. Multiple Infineon Wireless Module Partners are in production for fast time-to-market, for complete list please see the Infineon Wi-Fi Bluetooth ® Partner Module Product Selector Guide or visit the AIROC™ 54591X webpage.
AIROC™ CYW5459x Benefits
IEEE Wi-Fi 5 802.11a/b/g/n/ac-compliant Wi-Fi w/ 2X2 MIMO provides Best interoperability with access points delivers seamless high definition video/audio experience
Advanced co-existence engine allows for optimal Wi-Fi and Bluetooth® performance
Dual-Mode Bluetooth® 5.3 to support Long Range, high-speed (2Mbps) and Advertising Extensions
High speed interfaces PCIe 3.0 and SDIO for reduced latency
Tighter pitch package WLBGA .40nm for low cost chip on board designs
Wi-Fi Features:
Wi-Fi 5 (802.11ac), Dual-band (2.4/5 GHz)
Dual MAC Architecture: 2x2 MIMO or 1+1 RSDB modes (CYW54950 Only)
RSDB supports simultaneous 2.4GHz & 5GHz operation
20/40/80 MHz channels, up to 867MHz PHY data rate
MU-MIMO (Wave 2) support in STA mode
Internal PA and LNA w/ support for external PA/LNAs
PCle Gen1 (3.0 compliant), SDIO host interface
UART for Bluetooth® ®, 12S/PCM for Bluetooth® audio
Bluetooth® Features:
Class 1 (100 m) and Class 2 (10 m) operation
Bluetooth® 5.3 (BR + EDR + Bluetooth® LE): Supports LE-2Mbps, LE-Long Range, LE-Advertising Extension
Dedicated Bluetooth® path for best Coex performance
General Features:
Supports two concurrent data streams using Real Simultaneous Dual Band
Key Features
For more information, please go to: AIROCCYW5459x

## Slide 2: AIROC™ CYW54590/54591 Dual-Band Wi-Fi 5 + Bluetooth® Combo SoC Reliable solution for IoT applications needing Wi-Fi 5
Product brief
Product summary
Name | Description | Temperature range [°C] | Package
CYW5459x | Dual-Band Wi-Fi 5 + Bluetooth® Combo SoC | -40C to +85C | 194-ball WLBGA (5.16 mmx 7.7mm, 0.4mm pitch)
CYW54591: Murata Type 1XA (LBEE5XV1XA) | Fully certified Murata Module integrating the AIROC™ Dual-Band Wi-Fi 5 + Bluetooth® Combo SoC | -40C to +85C | 11.4 (Typ.) x 8.9 (Typ.) x 1.40 (Max.) Solder bump height = 0.04 (Typ.)
CYW54591: Murata Type 2XZ (LBEE5XV2XZ) | Fully certified Murata Module integrating the AIROC™ Dual-Band Wi-Fi 5 + Bluetooth® Combo SoC | -40C to +85C | 11.4 (Typ.) x 8.9 (Typ.) x 1.40 (Max.) Solder bump height = 0.04 (Typ.)
CYW54590: Murata Type 2BZ (LBEE5XV2BZ) | Fully certified Murata Module integrating the AIROC™ Dual-Band Wi-Fi 5 + Bluetooth® Combo SoC | -40C to +85C | 11.4 (Typ.) x 8.9 (Typ.) x 1.40 (Max.) Solder bump height = 0.04 (Typ.)
CYW54590: Murata Type 2BA (LBEE5XV22BA) | Fully certified Murata Module integrating the AIROC™ Dual-Band Wi-Fi 5 + Bluetooth® Combo SoC | -40C to +85C | 11.4 (Typ.) x 8.9 (Typ.) x 1.40 (Max.) Solder bump height = 0.04 (Typ.)
CYW54590: AzureWave (CM590) | 2x2 dual-band 2.4 GHz and 5 GHz Wi-Fi 5 (802.11ac) and Bluetooth® 5.3. In IEEE 802.11ac mode | -40C to +85C | 13 x 15mm
CYW54591: Azurewave (AW-CB511NF) | Offers Real Simultaneous Dual Band functionality enabling 1x1 connections on both the 2.4 GHz and 5 GHz bands at the same time | -40C to +85C | 22 x 30 x 2.25mm
CYW54591: Azurewave (AW-CM572) | Offers Real Simultaneous Dual Band functionality enabling 1x1 connections on both the 2.4 GHz and 5 GHz bands at the same time | -40C to +85C | 22 x 30 x 2.25mm
Quectel FC80A | Establishes WLAN & Bluetooth connections. 2×2 MIMO and 1×1+1×1 RSDB supported & provides maximum theoretical data rate up to 866.6Mbps | -30°C to +75°C | 15mm × 13mm × 2.2mm
Key applications
High Definition Video Streaming | Digital Signage, Video Surveillance
Smart Home | Smart Speakers, Gaming, Virtual Reality, Smart TV, Multi-Room Speakers
Networking Throughput | Gateways, Edge Computing, WLAN, Datacenter
Document number: 002-36003
Date: 07/2022