## Slide 1: LITIX™ Linear TLD1211SJ
October 2020

## Slide 2: TLD1211SJ only needs one sense resistor to realize your LED light
Features:
  Maximum operating voltage: 28 V
  Current range: 10 mA – 85 mA in “stand alone” mode
    Need of only one sense resistor
  Short circuit protection
  Temperature dependent output current reduction
  Low current consumption during Open Load, typ. 1.4 mA
  PWM over EN-pin
PG-DSO-8

## Slide 3: TLD1211SJ acts as controller and provides a high current solution
The TLD1211SJ is capable of driving high currents up to 2.5 A by using additional external output stages as “booster” transistors
Depending on the total power dissipation, more transistors in parallel can be used to split the power dissipation (better heat distribution with spread hot spots on the PCB)

## Slide 4: Application example: rear fog light with TLD1211SJ
Stable and reliable LED brightness
Protection features prevent damage to the device
Temperature dependent current reduction protects the LEDs from damage
Low current consumption during Open Load condition
Better thermal management; possibility to offload power dissipation to more parallel transistors when used in applications with high total power dissipation
Application Description & Block Diagram
LITIX™ Linear TLD1211SJ Benefits
Fog: 3 LEDs, 250 mA
Diagnosis is not required
Protection features: short circuit, over-temperature, overload, overvoltage

## Slide 5: Support Material to ease your design-in of TLD1211SJ
OrCAD
SIMetrix
MicroCap
TLD1211SJ_EVAL
Infineon‘s automotive solutions for rear LED lighting
LITIX™ Solutions for automotive rear lighting architectures
Simulation Models
Evaluation Boards
Online Trainings
New

## Slide 6: TLD1211SJ_EVAL evaluation board
Equipped with one LITIX™ Linear TLD1211SJ
Typical supply voltage range 8V – 16V
Two possible output current configurations:
  IOUT = 50 mA
  IOUT = 300 mA
On-board LEDs for easy evaluation