## Slide 1: Product Presentation IRF150DM115 Technology: 150 V OptiMOS™ 5 Package: DirectFET™ MN Outline
May 2024

## Slide 2: Table of contents
Introduction
1
  3
Application overview
2
  5
DirectFET™ advantages
3
  7
Application testing
4
  10
Summary
5
  14

## Slide 3: Table of contents
Introduction
1
3
Application overview
2
  5
DirectFET™ advantages
3
  7
Application testing
4
  10
Summary
5
  14

## Slide 4: OptiMOS™ 5 150 V in DirectFET™ MN Outline
Product features
Double-side cooled package
Low parasitic inductance
Low profile design
High current capability
100% lead-free (RoHS compliant)
Key parameters
Ag-filled epoxy die attach
Silicon die
Cu can
Pre-solder bumps
DirectFETTM cooling area
23.7mm² with 0.5m TIM
14.6mm2 without TIM
Part number | OPN | VDS (V) | RDS(on) max. @VGS = 10 V (m) | Qg typ (nC) | package | Product status
IRF150DM115 | IRF150DM115XTMA1 | 150 | 11.3 | 33 | DirectFET™ MN Outline | Mass production
Product benefits
Enables designs with high power density
High efficiency
Minimized EMI
Optimized thermals
Board space reduction
Less device paralleling
DirectFET™ package - MN Outline

## Slide 5: Table of contents
Introduction
1
  3
Application overview
2
5
DirectFET™ advantages
3
  7
Application testing
4
  10
Summary
5
  14

## Slide 6: Target applications Dual-side cooling and small form factor  compactness
Power optimizer MPPT – Booster
B6 topology
B6 topology

## Slide 7: Table of contents
Introduction
1
  3
Application overview
2
  5
DirectFET™ advantages
3
7
Application testing
4
  10
Summary
5
  14

## Slide 8: OptiMOS™ 5 150 V in DirectFET™ MN Outline Volume and area optimisation
5 x 6.3 x 0.7 mm
Area: 32.1 mm2
Vol.: 22.4 mm3
7 x 9.1 x 0.7 mm
Area: 63.7 mm2
Vol.: 44.6 mm3
6.7 x 10.4 x 2.4 mm
Area: 70.1 mm2
Vol.: 166 mm3
Top view
M-can
L-can
D-PAK
D2PAK
6.7 x 10.4 x 2.4 mm
Area: 70.1 mm2
Vol.: 166 mm3
54% area reduction
87% vol. reduction
9% area reduction
73% vol. reduction
63% area reduction
95% vol. reduction
81% area reduction
97% vol. reduction

## Slide 9: OptiMOS™ 5 150 V in DirectFET™ MN Outline 100% Pb free and RoHS 6 compliant!
100% Pb free pre-solder pad
Uses epoxy as die attach material
DirectFET™ is a high-volume proven and high power package which is already RoHS 6 compliant!
DirectFET™

## Slide 10: Table of contents
Introduction
1
  3
Application overview
2
  5
DirectFET™ advantages
3
  7
Application testing
4
10
Summary
5
  14

## Slide 11: Application test Series synchronous buck converter test setup
Test conditions:
Input voltage: 200 V
Load current: up to 27 A (~3 kW) with heatsink
Switching frequency: 40 kHz
Deadtime: 100 ns
Duty cycle: 56%
Part:
IRF150DM115
Power supply
Load
12V Supply
Test board
Thermal camera
Oscilloscope
Test Board

## Slide 12: Application test High-side turn-ON – smooth switching behavior
HS Top Vds 50V/div: 100.2V
HS Bot Vgs 5V/div
HS Top Vgs 5V/div
1.58V
1.04V
HS Bot Vds 50V/div: 101.9V
LS Top Vgs 5V/div
LS Bot Vgs 5V/div
LS Top Vds 50V/div: 102.6V
LS Bot Vds 50V/div: 101.4V
DFET @ 27A Load Current
Rgon: 30Ω / Rgoff: 1Ω
Schematic
HS Top x3
HS Bot x3
LS Top x3
LS Bot x3

## Slide 13: Application test Temperature performance
DFET @ 27 A load current
Rgon: 30Ω / Rgoff: 1Ω
77oC
Part | Temp °C @ 18 A | Temp °C @ 25 A | Temp °C @ 27 A
IRF150DM115 | 61.2 | 73.8 | 77
Part | Temp °C @ 18 A | Temp °C @ 25 A | Temp °C @ 27 A
IRF150DM115 | 92.1 | 73.8 | 77
Without heatsink
With heatsink
Input Voltage: 200 V
Load Current: up to 27 A (~3 kW) with heatsink
Switching Frequency: 40 kHz
Deadtime: 100 ns
Duty cycle: 56%
Test conditions:

## Slide 14: Table of contents
Introduction
1
  3
Application overview
2
  5
DirectFET™ advantages
3
  7
Application testing
4
  10
Summary
5
14

## Slide 15: OptiMOS™ 5 150 V in DirectFET™ MN Outline Summary
Surface mounted dual side cooled package enabling compact designs
Addressing multiple applications and topologies
RoHS 6 compliant