## Slide 1
Small Signal/Small Power MOSFET
for the Industrial Market
Sabrina Lindtner-Ascherle (PSS PD DCDC ULVS)
March 2021

## Slide 2: Agenda
New Small Signal/Small Power MOSFETs for Industrial market
Support material
1
2

## Slide 3: Small Signal/Small Power
The term Small Signal/Small Power MOSFET at Infineon refers to products in SOT packages such as SOT-223, SOT-23, SOT-323, SOT-363, and also includes TSOP-6 and SC59.
A Small Signal/Small Power MOSFET from Infineon is the same as any other MOSFET with an RDS(on), a breakdown voltage and a current rating. The parts are suitable for applications where low power is required. They allow full functionality by saving printed circuit board space.
„Small Signal is everywhere“

## Slide 4: Small Signal/Small Power MOSFET
Infineon offers a broad Small Signal/ Small Power portfolio with AEC-Q101 Qualified products in a variety of packages
Automotive Small Signal
Industrial Small Signal
Infineon offers a new Small Signal/Small Power portfolio with Industrial Qualified products in SOT-23 and SOT-223 packages
In this presentation the focus is on the Small Signal/Small Power Industrial portfolio
For more information visit the Infineon webpage: www.infineon.com/smallsignalmosfets
Notes: *MGD = MOS Gated Diode = Integrated schottky like diode

## Slide 5: Agenda
New Small Signal/Small Power MOSFETs for Industrial market
Support material
1
2

## Slide 6
NEW Small Signal/Small Power MOSFETs for the
Industrial Market
New

## Slide 7: Small Signal/Small Power MOSFET Product Portfolio focusing on the Industrial Market segment
OptiMOS™ N-channel
N-channel MOSFETs for best fit price/performance ratio
  Achieving excellent price/performance ratio and availability are the key requirements for consumer and industrial market segments
Motivation
Small Signal and Small Power products in SOT23 and SOT223 packages
8 new Small Signal/Small Power products
Product description
Broader portfolio to address industrial customers
Best fit for price/performance products
Infineon brand and quality
Benefits
Packages | 
SOT223 6.5x7.0x1.6 | SOT23 2.9x2.4x1.0
New
N-channel |  |  |  | 
Voltage class | Package | Part number | RDS(on) max. @ VGS= 10 V [m] | Release date
60 V | SOT-23 | 2N7002 | 3000 | released
 |  | BSS138I | 3500 | 
 |  | SN7002I | 5000 | 
100 V |  | BSS123I | 6000 | 
 |  | BSS169I | 6000 | 
250 V |  | BSS139I | 14000 | 
600 V |  | BSS127I | 500000 | 
 | SOT-223 | BSP135I | 45000 | 

## Slide 8: Small Signal/Small Power MOSFET Product Portfolio focusing the Industrial Market segment
OptiMOS™ P-channel
P-channel MOSFETs for best fit price/performance ratio
  Achieving excellent price/performance ratio is the key requirement for consumer and industrial applications
Motivation
OptiMOS™ P-channel -60 V is the new technology targeted for battery management, load switch and reverse polarity protection applications
Product description
P-channel |  |  |  | 
Voltage class | Package | Part number | RDS(on) max. @ VGS= 10 V [m] | Release date
-60 V | SOT-223 | ISP650P06NM | 65 | released
 |  | ISP12DP06NM | 125 | 
 |  | ISP25DP06LM | 250 | 
 |  | ISP25DP06NM | 250 | 
 |  | ISP75DP06LM | 750 | 
 | SOT-23 | ISS17EP06LM | 1700 | 
 |  | ISS55EP06LM | 5500 | 
Energy efficiency
Improved efficiency at low loads due to low Qg
Fast switching
Benefits
Packages | 
SOT223 6.5x7.0x1.6 | SOT23 2.9x2.4x1.0

## Slide 9: Key Features and Benefits
Small outline packages
PCB space and cost savings
Gate drive flexibility
High overall efficiency
Enables robust design
Industry standard qualification level
Key Features
Key Benefits
Value
High performance
Compact solution
Ease of design
Enhancement Mode and Depletion Mode options
Qualified according to JEDEC for Industrial applications
Faster time to market
Fast switching

## Slide 10: Application Example: Auxiliary circuits for Digital IC
HIGH Voltage
Load
Vcharge
Li
cell
USB
POWER
Micro Controller
Signal Out
Vin
Signal Out
Sense
Select
5V
Adapter
Buffer
&
Level Shifter
Charger
(LDO)
Power
Switch
Discrete
Logic Circuit
Power Switch, Charger(LDO)
Products Package Ptotal (W)
ISP650P06NM SOT-223 4.2
ISP12DP06NM SOT-223 4.2
ISP25DP06LM SOT-223 5.0
ISP25DP06NM SOT-223 4.2
ISP75DP06LM SOT-223 4.2
Products Package Ptotal (W)
ISS17EP06LM SOT-23 0.36
ISS55EP06LM SOT-23 0.4
2N7002 SOT-23 0.5
BSS138I SOT-23 0.36
SN7002I SOT-23 0.36
BSS123I SOT-23 0.5
BSS127I SOT-23 0.5
Buffer, Level Shifter
Discrete Logic Circuit
Product Example

## Slide 11: Application Example: Depletion MOSFET Use Case
Vin
Micro
Controller
Start-up Circuit
Vin
Constant Current Drive
Start-up Circuit
Constant Current Drive
Product Example
Products Package Ptotal (W)
BSS169I SOT-23 0.36
BSS139I SOT-23 0.36
BSP135I SOT-223 1.8

## Slide 12: Agenda
New Small Signal/Small Power MOSFETs for Industrial market
Support material
1
2

## Slide 13: Support Small Signal and Small Power MOSFET
  Product Briefs
  Selection Guides
  Application Brochures
  Presentations
  Press Releases
  Collaterals and Brochures
  Technical Material
  Videos
  Application Notes
  Technical Articles
  Datasheets
  Technical Information
  Product Information
  Small Signal / Small Power MOSFET
  Power MOSFET
  Depletion MOSFET
  Complementary MOSFET
  Power and Sensing Selection Guide

## Slide 14: Support Online Tools and Services
  Tools, Finders and Selectors
  Support
  Subscribe to Newsletter
3
4
1
1
3
4
  Where to Buy
2
2

## Slide 15: Tailor made information via myInfineon
Use the form to self-register (type in necessary information)
A confirmation email with the activation link is sent to you, please click on the link to activate your account
Log in to myInfineon
From the infineon.com go to the registration page
In case of problems with the access, the registration or all other type of issues, please get in touch with your Infineon contact person or with our official support at www.infineon.com/support (available 24/7)