## Slide 1
Sales Presentation
High Power DP4T Cross Switch for 5G sub-6GHz BGSX24MU16
November 2019

## Slide 2: Antenna Cross Switches Portfolio overview
Part Number | Type | IL@2.7GHz (dB) | Frequency (GHz) | Control | Size (mm2) | Status
BGSX22G2A10 | DPDXT | 0.43 | 0.1 – 3.8 | GPIO | 1.15 x 1.55 | MP (For new designs: BGSX22G5A10)
BGSX22G5A10 | DPDXT | 0.40 | 0.1 – 6.0 | GPIO | 1.1 x 1.5 | MP
BGSX33MU16 | 3P3XT | 0.50 | 0.1 – 3.8 | MIPI 2.0 | 2.0 x 2.0 | MP
BGSX24MU16 | DP4XT | 0.60 | 0.1 - 5.0 | MIPI 2.1 | 2.0 x 2.0 | MP
As of Nov, 2019

## Slide 3: High Power DP4T Cross Switch for 5G sub-6GHz BGSX24MU16
DP4T Antenna Cross Switch with high linearity up to 36.5 dBm
Suitable for smart routing/swapping antennas
Quadruple antenna applications
Post PA power level routing switch
Multimode LTE
2.0 x 2.0 mm2
(ULGA)
Package
Features & Applications
Block Diagram
Pinning (Top View)
Values | f [GHz] | IL [dB] | ISO [dB]
BGSX24MU16 | 0.7 – 1.0 | 0.40 | 49
 | 2.3 – 2.7 | 0.60 | 42
 | 3.8 – 5.0 | 1.00 | 40
New

## Slide 4: DP4T BGSX24MU16 5G/LTE Dual Connectivity Implementation Scenario
DP4T
N41 Tx/Rx
B7/B3 Tx/Rx
RFFE
ANT1
ANT2
ANT3
ANT4
5G SRS Support
This approach supports DC with LTE (e.g. B3/B7) + 5G (n41) working at the same time
Furthermore it supports 5G SRS (Tx) on all 4 antennas
BGSX24MU16

## Slide 5: DP4T BGSX24MU16 5G bands n77/n79 Implementation Scenario
DP4T
5G RFFE
n77, n79
n77, n79
n77, n79
n77, n79
DPDT
DPDT
Rx
Rx
BGSX22G5A10
BGSX22G5A10
BGSX24MU16

## Slide 6: BGSX24MU16 Highest ISO for 5G sub-6 GHz application
 | Qorvo QM11124 | Infineon DP4T x-switch BGSX24MU16
Size [mm] | 2.0 x 2.0 | 2.0 x 2.0
Ctrl interface | MIPI 2.1 | MIPI 2.1
Input Power [dBm max.] | 40 | 38
Insertion Loss [dB] typ. @5.0GHz | 0.9 | 1.0
Isolation [dB] typ. @5.0GHz | Lower than 30 | 40
P2P
*Qorvo QM1124 is pin-2-pin (P2P) with IFX BGSX24MU16. Note that QM1124 VDD+VIO is in same pin while IFX BGSX24MU16 has them in seperate pins. Only pin 9 is different.

## Slide 7: Support RF Switches
  www.infineon.com/mediacenter
  RF & Wireless Control
  RF Switches at Infineon.com
  Product Briefs
  Selection Guides
  Application Brochures
  Presentations
  Press Releases, Ads
  Collaterals and Brochures
  Technical Material
Videos/
Distribution Trainings
  Application Guide for Mobile Communication
  Videos
  Application Notes
  Technical Articles
  Simulation Models
  Datasheets, MCDS Files
  PCB Design Data
  Evaluation Boards
  Demo boards
  Reference Designs
Contact
  Technical assitance
  Submit your questions at our Technical Assistance Center

## Slide 8: Support Online tools and services
  Tools, Finders and Selectors
  Support
  Subscribe to Newsletter
3
4
1
1
3
4
  Where to Buy
2
2

## Slide 9: My Infineon